ORDINANCE NO.   2020-0-30

AN ORDINANCE ENACTING A GENERAL PRETREATMENT PROGRAM REGULATING USE OF SEWERS AND PROVIDING PENALTIES FOR VIOLATIONS

THEREOF IN THE CITY OF ROBINSON, CRAWFORD COUNTY, ILLINOIS

BE IT ORDAINED by the City Council of the City of Robinson, Crawford County, Illinois, as follows:

SECTION 1 - GENERAL PROVISIONS

1.1	Purpose and Policy

This ordinance sets forth uniform requirements for users of the Publicly Owned Treatment Works for the City of Robinson, Illinois and enables the City to comply with all applicable State and Federal laws, including the Clean Water Act (33 United States Code § 1251 et seq.), The Environmental Protection Act (415 ILCS 5/1 et seq), 35 Ill. Adm. Code, Subtitle C, and the General Pretreatment Regulations (40 Code of Federal Regulations Part 403). The objectives of this ordinance are:

A. To prevent the introduction of pollutants into the Publicly Owned Treatment Works that will

interfere with its operation;

B. To prevent the introduction of pollutants into the Publicly Owned Treatment Works that will

pass through the Publicly Owned Treatment Works, inadequately treated, into receiving

waters, or otherwise be incompatible with the Publicly Owned Treatment Works;

C. To protect both Publicly Owned Treatment Works personnel who may be affected by wastewater and sludge in the course of their employment and the general public;

D. To promote reuse and recycling of industrial wastewater and sludge from the Publicly Owned

Treatment Works;

E. To provide for fees for the equitable distribution of the cost of operation, maintenance, and

improvement of the Publicly Owned Treatment works; and

F. To enable the city to comply with its National Pollutant Discharge Elimination System permit

conditions, sludge use and disposal requirements, and any other Federal or State laws to

which the Publicly Owned Treatment works is subject.

This ordinance shall apply to all users of the Publicly Owned Treatment Works.   The

ordinance authorizes the  issuance of wastewater discharge permits; provides for monitoring.

compliance, and enforcement activities;  establishes administrative review procedures; requires

user reporting; and provides for the setting of fees for the equitable distribution of costs resulting

from the program established herein.

1.2	Administration

Except as otherwise provided herein, the superintendent shall administer, implement, and

enforce the  provisions  of  this ordinance.   Any powers granted to or duties imposed upon the

Superintendent may be delegated by the Superintendent to duly authorized city personnel.

1.3	Abbreviations

The following abbreviations, when used in this ordinance, shall have the designated meanings:

BOD - Biochemical Oxygen Demand

BMP – Best Management Practices

BMR – Baseline Monitoring Report

CFR - Code of Federal Regulations

CIU – Categorical Industrial User

COD - Chemical Oxygen Demand

USEPA - U.S. Environmental Protection Agency

gpd - gallons per day

IU – Industrial User

mg/L - milligrams per liter

NPDES - National Pollutant Discharge Elimination System

NSCIU – Non-Significant Categorical Industrial User

POTW	- Publicly Owned Treatment Works

RCRA - Resource Conservation and Recovery Act Standard Industrial Classification

SIU – Significant Industrial User

SNC – Significant Noncompliance

TSS - Total Suspended Solids

U.S.C. - United States Code

1.4	Definitions

Unless a provision explicitly states otherwise, the following terms and phrases, as used in this

ordinance,  shall have the meanings hereinafter designated.

A.	Act or  “the Act.”  The Federal Water Pollution Control Act, also known as the Clean

Water Act, as amended, 33 U.S.C. § 1251 et Seq;

B.        Approval Authority.  Regional Administrator, Region 5, The  United  States

Environmental  Protection  Agency (USEPA).

C.	Authorized Representative of the User.

(1.)  If the user is a corporation:

(a) The president, secretary, treasurer, or a vice-president of the corporation in

charge of a principal business function , or any other person who performs

similar policy or decision-making functions for the corporation ; or to the

manager in accordance with corporate procedures.

(b) The manager of one or more manufacturing, production, or operation facilities

employing  more than two hundred fifty (250) persons or having gross annual

sales or expenditures exceeding twenty-five (25) million dollars (in second-

quarter 1980 dollars), if authority to sign documents has been assigned or

delegated to manager in accordance with corporate procedures.

(c)  If the user is a partnership or sole proprietorship: a general partner or proprietor.

respectively

(d)  If the user is a Federal, State, or local governmental facility: a director or highest

official appointed or designated to oversee the operation and performance of the

activities of the government facility, or their designee.

(e)  The individuals described in paragraphs 1 through 3. above, may designate

another authorized representative if the authorization is in writing, the

authorization specifies the individual or position responsible for the overall

operation of the facility from which the discharge originates or having overall

responsibility for environmental matters for the company, and the written

authorization is submitted to the City.

(2.) If the User is a partnership or sole proprietorship: a general partner or proprietor,

respectively.

(3.) If the User is a Federal, State, or local governmental facility:  a director or highest

official appointed or designated to oversee the operation and performance of the

activities of the government facility, or their designee.

(4) The individuals described in paragraphs 1 through 3, above, may designate a Duly

Authorized Representative if the authorization is in writing, the

authorization specifies the individual or position responsible for the overall operation

of the facility from which the discharge originates or having overall responsibility for

environmental matters for the company, and the written authorization is submitted to

the City.

D.	Biochemical Oxygen Demand or BOD. The quantity of oxygen utilized in the

biochemical oxidation of organic matter under standard laboratory procedures for five (5)

days at 20 centigrade, usually expressed as a concentration (e.g., mg/L).

E.        Best Management Practices or BMPs means schedules of activities, prohibitions of

practices, maintenance procedures, and other management practices to implement the

prohibitions listed in Section 2.1 A and B [40 CFR 403.5(a)(1) and (b)]. BMPs include

treatment requirements, operating procedures, and practices to control plant site runoff,

spillage or leaks, sludge or waste disposal, or drainage from raw materials storage.

F.         Bypass [40 CFR 403.17(a)] The intentional diversion of wastestreams from any portion

of an industrial user’s treatment facility.

G.        Categorical pretreatment standards [paraphrased from 40 CFR 403.6] Standards

specifying the quantity, concentration, or pollutant properties of pollutants that may be

discharged to POTWs. EPA promulgates pretreatment standards for specific industry

categories in accordance with CWA section 307. These standards are codified in 40 CFR

chapter I, subchapter N, Parts 405–471.

H.        Categorical Industrial User.  An Industrial User subject to a categorical Pretreatment

Standard or categorical Standard.

I.         Chemical Oxygen Demand or COD.  A measure of the oxygen required to oxidize all

compounds, both organic and inorganic, in water.

J.	City.  The City of Robinson Illinois.

- Daily Maximum.  The arithmetic average of all effluent samples for a pollutant collected

during a calendar day.

L.	Environmental Protection Agency or USEPA. The U.S. Environmental Protection

Agency or, where appropriate, the Regional Water Management Division Director, or

other duly authorized official of said agency.

M.	Existing Source.    Any source of discharge that is not a “New Source.”

N.	Grab Sample.  A sample which is taken from a wastestream without regard to the flow in

the wastestream and over a period of time not to exceed fifteen (15) minutes.

O.	Indirect Discharge or Discharge. The introduction of pollutants into the POTW from any

nondomestic source regulated under Section 307(b), (c), or (d) of the Act.

P.	Instantaneous Maximum Allowable Discharge Limit. The maximum concentration of a

pollutant allowed to be discharged at any time, determined from the analysis of any

discrete or composited sample collected, independent of the industrial flow rate and the

duration of the sampling event.

Q.	Interference.  A discharge, which alone or in conjunction with a discharge or discharges

from other sources, inhibits or disrupts the POTW, its treatment processes or operations

or its sludge processes, use or disposal; and therefore, is a cause of a violation of the

City's NPDES permit or of the prevention of sewage sludge use or disposal in compliance

with any of the following statutory/regulatory provisions or permits issued thereunder, or

any more stringent State or local regulations: Section 405 of the Act: the Solid Waste

Disposal Act, including Title II commonly referred to as the Resource Conservation and

Recovery Act (RCRA); any State regulations contained in any State sludge management

plan prepared pursuant to Subtitle D of the Solid Waste Disposal Act; the Clean Air Act;

the Toxic Substances Control Act; and the Marine Protection, Research, and Sanctuaries

Act.

R.        Local Limit.  Specific discharge limits developed and enforced by the City upon

industrial or commercial facilities to implement the general and specific discharge

prohibitions listed in 40 CFR 403.5(a)(1) and (b).

S.         Medical Waste. Isolation wastes, infectious agents, human blood and blood products,

pathological wastes, sharps, body parts, contaminated bedding, surgical wastes,

potentially contaminated laboratory wastes, and dialysis wastes.

T.         Monthly Average.  The sum of all “daily discharges” measured during a calendar month

divided by the number of “daily discharges” measured during that month.

U.         Monthly Average Limit. The highest allowable average of “daily discharges”

over a calendar month, calculated as the sum of all “daily discharges” measured

during a calendar month divided by the number of “daily discharges” measured

during that month.

V.          National Pollutant Discharge Elimination System (NPDES) The national

program for issuing, modifying, revoking, and reissuing, terminating, monitoring,

and enforcing discharge permits from point sources to waters of the United

States, and imposing and enforcing pretreatment requirements, under CWA

sections 307, 402, 318, and 405.

W.	  New  Source. Any building, structure, facility, or installation from which there is (or

may be) a discharge of pollutants, the construction of which commenced after the

publication of proposed pretreatment standards under Section 307(c) of the Act which

will be applicable to such source if such standards are thereafter promulgated in

accordance with that section, provided that:

(a) The building, structure, facility, or installation is constructed at a site at which no

other source is located; or

(b) The building, structure, facility, or installation totally replaces the process or

production equipment that causes the discharge of pollutants at an existing

source; or

(c) The production or wastewater generating processes of the building, structure,

facility, or installation are substantially independent of an existing source at the

same site. In determining whether these are substantially independent, factors

such as the extent to which the new facility is integrated with the existing plant,

and the extent to which the new facility is engaged in the same general type of

activity as the existing source, should be considered.

(2)	Construction on a site at which an existing source is located results in a modification

rather than a new source if the construction does not create a new building, structure,

facility, or installation meeting the criteria of Section (1)(b) or (c) above but otherwise

alters, replaces, or adds to existing process or production equipment.

(3)	Construction of a new Source as defined under this paragraph has commenced if the

owner or operator has:

(a) Begun, or caused to begin, as part of a continuous onsite construction program

(i) any placement, assembly, or installation of facilities or equipment; or

(ii) significant site preparation work including clearing, excavation, or removal of

existing buildings, structures, or facilities which is necessary for the placement,

assembly, or installation of new source facilities or equipment; or

(b) Entered into a binding contractual obligation for the purchase of facilities or

equipment which are intended to be used in its operation within a reasonable time.

Options to purchase or contracts which can be terminated or modified without

substantial loss, and contracts for feasibility, engineering, and design studies do not

constitute a contractual obligation under this paragraph.

X.         Noncontact Cooling Water. Water used for cooling which does not come into direct

contact with any raw material, intermediate product, waste product, or finished product.

Y.         Nonsignificant Categorical Industrial User (NSCIU) [40 CFR 403.3(v)(2)] An IU subject

to categorical pretreatment standards under 40 CFR 403.6 and 40 CFR chapter I,

subchapter N, that the POTW has determined is exempt from the definition of SIU on a

finding that the IU never discharges more than 100 gpd of total categorical wastewater

(excluding sanitary, noncontact cooling and boiler blowdown wastewater, unless

specifically included in the pretreatment standard). The IU must also meet the following

conditions: The IU, before the POTW’s finding, has consistently complied with all

applicable categorical pretreatment standards and requirements.  The IU annually

submits the certification statement required in 40 CFR 403.12(q) together with any

additional information necessary to support the certification statement.  The IU never

discharges any untreated concentrated wastewater.

Z.         Pass Through.  A discharge which exits the POTW into waters of the United States in

quantities or concentrations which, alone or in conjunction with a discharge or discharges

from other sources, is a cause of a violation of any requirement of the City's NPDES

permit including an increase in the magnitude or duration of a violation.

AA.	Person.  Any individual, partnership, copartnership, firm, company, corporation,

association, joint stock company, trust, estate, governmental entity, or any other legal

entity; or their legal representatives, agents, or assigns.  This definition includes all

Federal, State, and local governmental entities.

BB.	pH.  A measure of the acidity or alkalinity of a solution, expressed in standard units.

CC.	Pollutant.  Dredged spoil, solid waste, incinerator residue, filter backwash, sewage,

garbage, sewage sludge, munitions, medical wastes, chemical wanes, biological

materials, radioactive materials, heat, wrecked or discarded equipment, rock, sand, cellar

dirt, municipal, agricultural and industrial wastes, and certain characteristics of

wastewater (e.g. pH, temperature, TSS, turbidity, color, BOD, COD, toxicity, or odor).

DD.     Pretreatment.  The reduction of the amount of pollutants, the elimination of pollutants, or

the alteration of the nature of pollutant properties in wastewater prior to, or in lieu of,

introducing such pollutants into the POTW. This reduction or alteration can be obtained

by physical, chemical, or biological processes; by process changes: or by other means,

except by diluting the concentration of the pollutants unless allowed by an applicable

pretreatment standard.

EE.	Pretreatment Requirements.  Any substantive or procedural requirement related to

pretreatment imposed on a user, other than a pretreatment standard.

FF.	Pretreatment Standards or Standards.  Pretreatment standards shall mean prohibited

discharge standards. categorical pretreatment standards, and local limits.

GG.	Prohibited Discharge Standards or Prohibited Discharges. Absolute prohibitions against

the discharge of certain substances; these prohibitions appear in Section 2.1 of this

ordinance.

HH.	Publicly Owned Treatment Works or POTW.  A “treatment works," as defined by

Section 212 of the Act (33 U.S.C.  § 1292) which is owned by the City. This definition

includes any devices or systems used in the collection, storage, treatment, recycling, and

reclamation of sewage or industrial wastes of a liquid nature and any conveyances which

convey wastewater to a treatment plant.

II.        Regional Administrator. Head of the office of the USEPA in Chicago, IL.

JJ.	Septic Tank Waste. Any sewage from holding tanks such as vessels, chemical toilets,

campers, trailers, and septic tanks.

KK.	Sewage.  Human excrement and gray water (household showers, dishwashing operations,

etc.)

LL.	Significant Industrial User.

(1) A user subject to categorical pretreatment standards: or

(2) A user that:

(a) Discharges an average of ten thousand (10,000) gpd or more of process wastewater

to the POTW (excluding sanitary, noncontact cooling, and boiler blowdown

wastewater);

(b)	Contributes a process wastestream which makes up five (5) percent or more

of the average dry weather hydraulic or organic capacity of the POTW

treatment plant;' or

(c)	Is designated as such by the City on the basis that it has a reasonable potential for

adversely affecting the POTW's operation or for violating any pretreatment

standard or requirement.

(3) Upon a finding that a user meeting the criteria in Subsection (2) has no reasonable

potential for adversely affecting the POTW's operation or for violating any

pretreatment standard or requirement. the City may at any lime, on its own initiative

or in response to a petition received from a user, and in accordance with procedures in

40 CFR 403.8(f)(6), determine that such user should not be considered a significant

industrial user.

MM.	Slug Load or Slug.  Any discharge at a flow rate or concentration, which could cause a

violation of the prohibited discharge standards in Section 2.1 of this ordinance.  A Slug

Discharge is any Discharge of a non-routine, episodic nature, including but not limited to

an accidental spill or a non-customary batch Discharge, which has a reasonable potential

to cause Interference or Pass Through, or in any other way violate the POTW’s

regulations, Local Limits or Permit conditions

NN.	Standard Industrial Classification (SIC) Code. A classification pursuant to the Standard

Industrial Classification Manual issued by the United States Office of Management and

Budget.

OO. 	Storm Water.  Any flow occurring during or following any form of natural precipitation.

and resulting from such precipitation, including snowmelt.

PP.	Superintendent. The person designated by the City to supervise the operation of the

P0TW and who is charged with certain duties and responsibilities by this ordinance, or a

duly authorized representative.

QQ. 	Suspended Solids. The total suspended matter that floats on the surface of, or is

suspended in water wastewater or other liquid, and which is removable by laboratory

filtering.

RR.     User or Industrial User.  A source of indirect discharge.

SS.	Wastewater.  Liquid and water-carried industrial wastes and sewage from residential

dwellings, commercial buildings, industrial and manufacturing facilities, and institutions,

whether treated or untreated, which are contributed to the POTW.

TT.	Wastewater Treatment Plant or Treatment Plant. That portion of the POTW which is

designed to provide treatment of municipal sewage and industrial waste.

1.5	Written Notice of Decisions

At least 15 days before the effective date of any decision to require additional pretreatment measures under section 3 of this Ordinance, to require the user to install monitoring equipment under Section 7 of this ordinance, or to require the reduction in flow or suspension of wastewater discharge under any Section other than Section 10.7 of this ordinance, the Superintendent shall provide the user with a written notice of his decision. The foregoing shall not excuse compliance with the provisions of this ordinance.

SECTION 2 - GENERAL SEWER USE REQUIREMENTS

2.1	Prohibited Discharge Standards

A.	General Prohibitions. No user shall introduce or cause to be introduced into the POTW

any pollutant or wastewater which causes pass through or interference. These

general prohibitions apply to all users of the POTW whether or not they are subject to

categorical pretreatment standards or any other National, State, or local pretreatment

standards or requirements.

B.	Specific Prohibitions. No user shall introduce or cause to be introduced into the POTW

the following pollutants, substances, or wastewater:

(1) Pollutants which create a fire or explosive hazard in the POTW, including, but

not limited to, wastestreams with a closed-cup flashpoint of less than 140º F

(60º C) using the test methods specified in 40 CFR 261.21:

(2) Wastewater having a pH less than 5.0 or more than 9.5, or otherwise causing

corrosive structural damage to the P0TW or equipment:

(3) Solid or viscous substances in amounts which will cause obstruction of the flow

in the POTW resulting in interference (but in no case solids greater than three

inches (3”) in any dimension);

(4) Pollutants, including oxygen-demanding pollutants (BOD, etc.), released in a

discharge at a flow rate and/or pollutant concentration which, either singly or

by interaction with other pollutants, will cause interference with the POTW;

(5) Wastewater having a temperature greater than 150º F, (65º C), or which will

inhibit biological activity in the treatment plant resulting in interference, but in

no case wastewater which causes the temperature at the introduction into the

treatment plant to exceed 104º F (40º C);

(6) Petroleum oil, nonbiodegradable cutting oil, or products of mineral oil origin, in

amounts that will cause interference or pass through:

(7) Pollutants which result in the presence of toxic gases, vapors, or fumes within

the POTW in a quantity that may cause acute worker health and safety

problems:

(8) Trucked or hauled pollutants, except at discharge points designated by the

Superintendent in accordance with Section 3.4 of this ordinance:

(9)  Noxious or malodorous liquids, gases, solids, or other wastewater which, either

singly or by interaction with other wastes, are sufficient to create a public

nuisance or a hazard to life, or to prevent entry into the sewers for maintenance

or repair:

(10) Wastewater which imparts color which cannot be removed by the treatment

process, such as, but not limited to, dye wastes and vegetable tanning solutions,

which consequently imparts color to the treatment plant’s effluent, thereby

violating the City's NPDES permit;

(11) Wastewater containing any radioactive wastes or isotopes except in compliance

with applicable State or Federal regulations;

(12) Storm water, surface water, ground water, artesian well water, roof runoff,

subsurface drainage, swimming pool drainage, condensate, deionized water,

noncontact cooling water, and unpolluted wastewater, unless specifically

authorized by the Superintendent;

(13) Sludges, screenings, or other residues from the pretreatment of

industrial wastes;

(14) Medical wastes, except as specifically authorized by the Superintendent in a

wastewater discharge permit;

(15) Wastewater causing, alone or in conjunction with other sources, the treatment

plant’s effluent to fail a toxicity test;

(16) Detergents, surface-active agents, or other substances which may cause

excessive foaming in the POTW;

(17) Fats, oils, or greases of animal or vegetable origin in concentrations greater

than one hundred (100) mg/L; or

(18) Wastewater causing two readings on an explosion hazard meter at the point of

discharge into the POTW, or at any point in the POTW, of more than five

percent (5%) or any single reading over ten percent (10%) of the lower

Explosive Limit of the meter.

Pollutants, substances, or wastewater prohibited by this section shall not be processed or

stored in such a manner that they could be discharges to the POTW.

2.2 National Categorical Pretreatment Standards

The categorical pretreatment standards found at 40 CFR Chapter I, Subchapter N, Parts 405-471 are hereby incorporated.

A.	Where a categorical pretreatment standard is expressed only in terms of either the mass or

the concentration of a pollutant in wastewater, the Superintendent may impose equivalent

concentration or mass limits in accordance with 40 CFR 403.6(c).

B.        When the limits in a categorical Pretreatment Standard are expressed only in terms of

mass of pollutant per unit of production, the Superintendent may convert the limits to

equivalent limitations expressed either as mass of pollutant discharged per day or

effluent concentration for purposes of calculating effluent limitations applicable to

individual Industrial Users.

C.       When wastewater subject to a categorical Pretreatment Standard is mixed with wastewater

not regulated by the same Standard, the Superintendent shall impose an alternate limit in

accordance with 40 CFR 403.6(e).

D.       A CIU may obtain a net/gross adjustment to a categorical Pretreatment Standard in

accordance with the following paragraphs of this Section.  [Note: See 40 CFR 403.15]

(1)	Categorical Pretreatment Standards may be adjusted to reflect the presence of

pollutants in the Industrial User’s intake water in accordance with this

Section. Any Industrial User wishing to obtain credit for intake pollutants

must make application to the City. Upon request of the Industrial User, the

applicable Standard will be calculated on a “net” basis (i.e., adjusted to reflect

credit for pollutants in the intake water) if the requirements of paragraph (2)

of this Section are met.

- Criteria.

  - Either (i) The applicable categorical Pretreatment Standards contained in 40 CFR subchapter N specifically provide that they shall be applied on a net basis; or (ii) The Industrial User demonstrates that the control system it proposes or uses to meet applicable categorical Pretreatment Standards would, if properly installed and operated, meet the Standards in the absence of pollutants in the intake waters.

  - Credit for generic pollutants such as biochemical oxygen demand (BOD), total suspended solids (TSS), and oil and grease should not be granted unless the Industrial User demonstrates that the constituents of the generic measure in the User’s effluent are substantially similar to the constituents of the generic measure in the intake water or unless appropriate additional limits are placed on process water pollutants either at the outfall or elsewhere.

c.	Credit shall be granted only to the extent necessary to meet the applicable categorical Pretreatment Standard(s), up to a maximum value equal to the influent value. Additional monitoring may be necessary to determine eligibility for credits and compliance with Standard(s) adjusted under this Section.

  - Credit shall be granted only if the User demonstrates that the intake water is drawn from the same body of water as that into which the POTW discharges. The City may waive this requirement if it finds that no environmental degradation will result.

E.  When a categorical Pretreatment Standard is expressed only in terms of pollutant

concentrations, an Industrial User may request that the City convert the limits to

equivalent mass limits. The determination to convert concentration limits to mass

limits is within the discretion of the Superintendent.  The City may establish

equivalent mass limits only if the Industrial User meets all the conditions set forth in

Sections 2.2E(1)(a) through 2.2E(1)(e) below.

- To be eligible for equivalent mass limits, the Industrial User must:

  - Employ, or demonstrate that it will employ, water conservation methods and technologies that substantially reduce water use during the term of its individual wastewater discharge permit;

  - Currently use control and treatment technologies adequate to achieve compliance with the applicable categorical Pretreatment Standard, and not have used dilution as a substitute for treatment;

  - Provide sufficient information to establish the facility’s actual average daily flow rate for all wastestreams, based on data from a continuous effluent flow monitoring device, as well as the facility’s long-term average production rate. Both the actual average daily flow rate and the long-term average production rate must be representative of current operating conditions;

  - Not have daily flow rates, production levels, or pollutant levels that vary so significantly that equivalent mass limits are not appropriate to control the Discharge; and

  - Have consistently complied with all applicable categorical Pretreatment Standards during the period prior to the Industrial User’s request for equivalent mass limits.

(2)  An Industrial User subject to equivalent mass limits must:

a.	Maintain and effectively operate control and treatment technologies adequate to achieve compliance with the equivalent mass limits;

b.	Continue to record the facility’s flow rates through the use of a continuous effluent flow monitoring device;

c.	Continue to record the facility’s production rates and notify the Superintendent whenever production rates are expected to vary by more than 20 percent from its baseline production rates determined in paragraph 2.2F(1)(c) of this Section.  Upon notification of a revised production rate, the Superintendent will reassess the equivalent mass limit and revise the limit as necessary to reflect changed conditions at the facility; and

d.	Continue to employ the same or comparable water conservation methods and technologies as those implemented pursuant to paragraphs 2.2E(1)(a) of this Section so long as it discharges under an equivalent mass limit.

(3)  When developing equivalent mass limits, the Superintendent:

- Will calculate the equivalent mass limit by multiplying the actual average daily flow rate of the regulated process(es) of the Industrial User by the concentration-based Daily Maximum and Monthly Average Standard for the applicable categorical Pretreatment Standard and the appropriate unit conversion factor;

- Upon notification of a revised production rate, will reassess the equivalent mass limit and recalculate the limit as necessary to reflect changed conditions at the facility; and

c.	May retain the same equivalent mass limit in subsequent individual wastewater discharger permit terms if the Industrial User’s actual average daily flow rate was reduced solely as a result of the implementation of water conservation methods and technologies, and the actual average daily flow rates used in the original calculation of the equivalent mass limit were not based on the use of dilution as a substitute for treatment pursuant to Section 2.6.  The Industrial User must also be in compliance with Section 13.3 regarding the prohibition of bypass.

F.  The Superintendent may convert the mass limits of the categorical Pretreatment Standards of 40 CFR Parts 414, 419, and 455 to concentration limits for purposes of calculating limitations applicable to individual Industrial Users.  The conversion is at the discretion of the Superintendent.

G. Once included in its permit, the Industrial User must comply with the equivalent limitations developed in this Section (2.2) in lieu of the promulgated categorical Standards from which the equivalent limitations were derived.  [Note: See 40 CFR 403.6(c)(7)]

H. Many categorical Pretreatment Standards specify one limit for calculating maximum daily discharge limitations and a second limit for calculating maximum Monthly Average, or 4-day average, limitations. Where such Standards are being applied, the same production or flow figure shall be used in calculating both the average and the maximum equivalent limitation. [Note: See 40 CFR 403.6(c)(8)]

I. Any Industrial User operating under a permit incorporating equivalent mass or concentration limits calculated from a production-based Standard shall notify the Superintendent within two (2) business days after the User has a reasonable basis to know that the production level will significantly change within the next calendar month. Any User not notifying the Superintendent of such anticipated change will be required to meet the mass or concentration limits in its permit that were based on the original estimate of the long term average production rate. [Note:  See 40 CFR 403.6(c)(9)]

2.3	State Pretreatment Standards

State requirements and limitations on discharges to the POTW shall be met by all dischargers which are subject to those standards in any instance in which they are more stringent than federal requirements and limitations or those in this or any other applicable ordinance.

2.4	Local Limits

No discharger shall discharge or cause or allow to be discharged into the sewerage system any pollutant in concentrations above those specifically permitted in a Wastewater Discharge Permit Issues by the City. Discharge Permits shall impose maximum discharge concentration limits or mass based limits where appropriate. The Superintendent may, upon good cause shown, establish wastewater permit limits below a local limit concentration set forth in this Section. In the absence of such specific wastewater discharge permit conditions, no person shall discharge any of the following pollutants except as such pollutants may occur, and only in the concentrations such pollutants may occur, in the potable water supplied to the premises.

0.10     mg/L arsenic

0.13     mg/L cadmium

0.27	mg/L chromium (hex)

0.70	mg/L chromium (total)

0.94	mg/L copper

0.91     mg/L cyanide

4.20    mg/L iron (total)

0.42	mg/L lead

0.0138    mg/L mercury

1.11	mg/L nickel

10.0	mg/L manganese

0.96    mg/L zinc

300       mg/L BOD

350       mg/L TSS

20       mg/L NH3-N

10       mg/L Phosphorus (total)

pH   Daily Min. 5.0 Daily Max 9.5

Oil & Grease Daily Max. 100 mg/L

Oil & Grease Weekly Avg. 80 mg/L

The above limits apply at the point where the wastewater is discharged to the POTW.  All concentrations for metallic substances are for total metal unless indicated otherwise.  The

Superintendent may impose mass limitations in addition to the concentration-based limitations above.

Discharge limits for BOD and TSS will be established in individual Wastewater Discharge Permits. For existing users, BOD and TSS limits will be established at or below currently allowed discharge levels. For new users or existing users with new production capacity discharging greater than 10,000 gpd, concentration limits will be set at levels that are economically achievable but not greater than 300 mg/L BOD5 and 350 mg/L TSS and such that treatment efficiency at the POTW will not be diminished.

Wastewater containing 5 day BOD greater than 300 mg/L, or TSS in excess of 350 mg/L, may be permitted by specific written agreement with the City provided the City has determined that no adverse effect on the City’s wastewater treatment facilities will occur from these alternative limits. Any written agreement with the City to discharge such BOD or TSS may provide for special charges, payments or provisions for treating and testing equipment.

The above limits apply at the point where the wastewater is discharged to the POTW. All concentrations for metallic substances are for “total” metal unless indicated otherwise. The Superintendent may impose mass limitations in addition to, or in place of, the concentrationbased limitations above.

SITE SPECIFIC RULES AND EXCEPTIONS NOT OF GENERAL APPLICABILITY

#### Hershey Chocolate USA, Robinson

a)	This Section applies only to wastewater discharges from Hershey Chocolate USA into the City of Robinson’s sanitary sewer collection system.

b)	Instead of the general effluent limitations set forth in Section 2.4 (Local Limits) for BOD5 and TSS, The limits shall be mass limits of;  BOD5 – 338 pound per day and TSS -  400 pounds per day.

2.5     City’s Right of Revision

The City reserves the right to establish, by Ordinance or in wastewater discharge permits,

more stringent standards or requirements on discharges to the POTW.

2.6	Dilution

No user shall ever increase the use of process water, or in any way attempt to dilute a

discharge, as a partial or complete substitute for adequate treatment to achieve compliance with a

discharge limitation.

SECTION 3- PRETREATMENT OF WASTEWATER

3.1 Pretreatmcnt Facilities

Users shall provide wastewater treatment as necessary to comply with this ordinance and

shall achieve compliance with all categorical pretreatment standards, local limits, and the

prohibitions set out in Section 2.1 of this ordinance within the time limitations specified by EPA,

the State, or the Superintendent, whichever is more stringent. Any facilities necessary for

compliance shall be provided, operated, and maintained at the user's expense. Detailed plans

describing such facilities and operating procedures shall be submitted to the Superintendent for

review, and shall be acceptable to the Superintendent before such facilities are constructed. The

review of such plans and operating procedures shall in no way relieve the user from the

responsibility of modifying such facilities as necessary to produce a discharge acceptable to the

City under the provisions of this ordinance.

3.2	Additional Pretreatment Measures

A.	Whenever deemed necessary, the Superintendent may require users to restrict their

discharge during peak flow periods, designate that certain wastewater be discharged only

into specific sewers, relocate and, or consolidate points of discharge, separate sewage

wastestreams from industrial wastestreams, and such other conditions as may be

necessary to protect the POTW and determine the user's compliance with the

requirements of this ordinance

B.	The Superintendent may require any person discharging into the POTW to install and

maintain, on their properly and at their expense, a suitable storage and flow-control

facility to ensure equalization of flow. A wastewater discharge permit may be issued

solely for flow equalization.

C.	Grease, oil, and sand interceptors shall be provided when, in the opinion of the

Superintendent, they are necessary for the proper handling of wastewater containing

excessive amounts of grease and oil, or sand; except that such interceptors shall not be

required for residential users. All interception units shall be of type and capacity

approved by the Superintendent and shall be so located to be easily accessible for

cleaning and inspection. Such interceptors shall be inspected, cleaned, and repaired

regularly, as needed, by the user at their expense.

D.	Users with the potential to discharge flammable substances may be required to install and

maintain an approved combustible gas detection meter.

3.3 	Accidental Discharge/Slug Discharge Control Plans

The Superintendent shall evaluate whether each SIU needs an accidental discharge/slug discharge control plan or other action to control Slug Discharges.  The Superintendent may require any User to develop, submit for approval, and implement such a plan or take such other action that may be necessary to control Slug Discharges.  Alternatively, the Superintendent may develop such a plan for any User.  An accidental discharge/slug discharge control plan shall address, at a minimum, the following:

- Description of discharge practices, including nonroutine batch discharges;

- Description of stored chemicals;

- Procedures for immediately notifying the Superintendent of any accidental or Slug Discharge, as required by Section 6.6 of this ordinance; and

- Procedures to prevent adverse impact from any accidental or Slug Discharge.  Such procedures include, but are not limited to, inspection and maintenance of storage areas, handling and transfer of materials, loading and unloading operations, control of plant site runoff, worker training, building of containment structures or equipment, measures for containing toxic organic pollutants, including solvents, and/or measures and equipment for emergency response.

3.4	Hauled Wastewater

A.  Septic tank waste may be introduced into the POTW only at locations designated by the Superintendent, and at such times as are established by the Superintendent.  Such waste shall not violate Section 2 of this ordinance or any other requirements established by the City.  The Superintendent may require septic tank waste haulers to obtain individual wastewater discharge permits.

B.  The Superintendent may require haulers of industrial waste to obtain individual wastewater discharge permits.  The Superintendent may require generators of hauled industrial waste to obtain individual wastewater discharge permits. The Superintendent also may prohibit the disposal of hauled industrial waste.  The discharge of hauled industrial waste is subject to all other requirements of this ordinance.

C.  Industrial waste haulers may discharge loads only at locations designated by the Superintendent.  No load may be discharged without prior consent of the Superintendent.  The Superintendent may collect samples of each hauled load to ensure compliance with applicable Standards.  The Superintendent may require the industrial waste hauler to provide a waste analysis of any load prior to discharge.

D.  Industrial waste haulers must provide a waste-tracking form for every load.  This form shall include, at a minimum, the name and address of the industrial waste hauler, permit number, truck identification, names and addresses of sources of waste, and volume and characteristics of waste.  The form shall identify the type of industry, known or suspected waste constituents, and whether any wastes are RCRA hazardous wastes.

The discharge of any hauled hazardous waste into the sanitary sewer system is strictly

prohibited. The discharge of any non-hazardous wastewater, including septic tank waste and

industrial waste into the sanitary sewer system or POTW is prohibited, unless prior written

approval is given by the Superintendent.

SECTION 4 - WASTEWATER DISCHARGE PERMIT APPLICATION

4.1	Wastewater Analysis

When requested by the Superintendent. a user must submit information on the nature and

characteristics of its wastewater within thirty (30) days of the request. The Superintendent Is

authorized to prepare a form for this purpose and may periodically require users to update this

information

4.2	Wastewater Discharge Permit Requirement

A.	No significant industrial user shall discharge wastewater into the POTW without first

obtaining a wastewater discharge permit from the Superintendent, except that a

significant industrial user that has filed a timely application pursuant to Section 4.3 of

this ordinance may continue to discharge for the time period specified therein.

B.	The Superintendent may require other users to obtain wastewater discharge permits as

necessary to carry out the purposes of this ordinance.

C.         Any violation of the terms and conditions of a wastewater discharge permit shall be

deemed a violation of this ordinance and subjects the wastewater discharge permittee to

the sanctions set out in Sections 10 through 12 of this ordinance. Obtaining a

wastewater discharge permit does not relieve a permittee of its obligation to comply with

all Federal and State pretreatment standards or requirements or with any other

requirements of Federal, State, and local law.

4.3	Wastewater Discharge Permitting: Existing Connections

Any user required to obtain a wastewater discharge permit who was discharging wastewater

into the P0TW prior to the effective date of this ordinance and who wishes to continue such

discharges in the future, stall, within sixty (60) days after said date, apply to the Superintendent

for a wastewater discharge permit in accordance with Section 4.5 of this ordinance, and shall not

cause or allow discharges to the POTW to continue after ninety (90) days of the effective date of

this ordinance except in accordance with a wastewater discharge permit issued by he

Superintendent.

4.4	Wastewater Discharge Permitting: New Connections

Any user required to obtain a wastewater discharge permit who proposes to begin or

recommence discharging into the POTW must obtain such permit prior to the beginning or

recommencing of such discharge. An application for this wastewater discharge permit, in

accordance with Section 4.5 of this ordinance, must be filed at least ninety (90) days prior to the

date upon which any discharge will begin or recommence.

4.5	Wastewater Discharge Permit Application Contents

All users required to obtain a wastewater discharge permit must submit a permit

application. The Superintendent may require all users to submit as part of an application the

following information:

A.	All information required by Section 6.1(B) of this ordinance;

B.	Description of activities, facilities, and plant processes on the premises, including a list of

all raw materials and chemicals used or stored at the facility which are, or could

accidentally or intentionally be, discharged to the POTW;

C.        Number and type of employees, hours of operation, and proposed or actual hours of

operation;

D.	Each product produced by type, amount, process or processes, and rate of production;

E.         Type and amount of raw materials processed (average and maximum per day);

F.	Site plans, floor plans, mechanical and plumbing plans, and details to show all sewers,

floor drains, and appurtenances by size, location, and elevation, and all points of

discharge;

G. 	Time and duration of discharges; and

H.	Any other information as may be deemed necessary by the Superintendent to evaluate the

wastewater discharge permit application.

I.         Any requests for a monitoring waiver (or a renewal of an approved monitoring waiver)

for a pollutant neither present nor expected to be present in the discharge based on

Section 6.4 B [40 CFR 403.12(e)(2)].

J.         Incomplete or inaccurate applications will not be processed and will be returned to the

user for revision.

4.6	Application Signatories and Certification

All wastewater discharge permit applications and user reports must be signed by an

authorized representative of the user and contain the following certification statement:

“I certify under penalty of law that this document and all attachments were prepared under

my direction or supervision in accordance with a system designed to assure that qualified

personnel properly gather and evaluate the information submitted. Based on my inquiry of

I the person or persons who manage the system, or those persons directly responsible for

gathering the information, the information submitted is, to the best of my knowledge and belief, true, accurate, and complete. I am aware that there are significant penalties for submitting false information, including the possibility of fine and imprisonment for knowing violations.”

If the designation of an Authorized Representative is no longer accurate because a different individual or position has responsibility for the overall operation of the facility or overall responsibility for environmental matters for the company, a new written authorization satisfying the requirements of this Section must be submitted to the Superintendent prior to or together with any reports to be signed by an Authorized Representative.

A facility determined to be a Non-Significant Categorical Industrial User by the Superintendent pursuant to 1.4 Y must annually submit the signed certification statement in Section 6.14 B. [Note: See 40 CFR 403.3(v)(2)]

4.7       Wastewater Discharge Permit Decisions

The Superintendent will evaluate the data furnished by the user and may require additional

information. Within thirty (30) days of receipt of a complete wastewater discharge permit

application, the Superintendent will determine whether or not to issue a wastewater discharge

permit. The Superintendent may deny any application for a wastewater discharge permit.

SECTION 5 - WASTEWASTER DISCHARGE PERMIT ISSUANCE PROCESS

5.1	Wastewater Discharge Permit Duration

A wastewater discharge permit shall be issued for a specified time period, not to exceed five

(5) years from the effective date of the permit. A wastewater discharge permit may he issued for

a period less than five (5) years, at the discretion of the Superintendent. Each wastewater

discharge permit will indicate a specific date upon which it will expire.

5.2	Wastewater Discharge Permit Contents

A wastewater discharge permit shall include such conditions as are deemed reasonably

necessary by the Superintendent to prevent pass through or interference, protect the quality of the

water body receiving the treatment plant's effluent, protect worker health and safety facilitate

sludge management and disposal, and protect against damage to the POTW.

A.	Wastewater discharge permits must contain:

(1)       A statement that indicates wastewater discharge permit duration, which in

no event shall exceed five (5) years.

(2)       A statement that the wastewater discharge permit is nontransferable

without prior notification to the City in accordance with Section 5.5 of

this ordinance, and provisions for furnishing the new owner or operator

with a copy of the existing wastewater discharge permit;

(3)      Self monitoring, sampling, reporting, notification, and record-keeping

requirements.  These requirements shall include an identification of

pollutants to be monitored, sampling location, sampling frequency. and

sample type based on Federal, State, and local law; and

(5)	The process for seeking a waiver from monitoring for a pollutant neither

present nor expected to be present in the Discharge in accordance with

Section 6.4 B.

(6)     A statement of applicable civil and criminal penalties for violation of

pretreatment standards and requirements, and any applicable compliance

schedule. Such schedule may not extend the time for compliance beyond

that required by applicable Federal, State, or local law.

(7)	Requirements to control Slug Discharge, if determined by the

Superintendent to be necessary.

(8)	Any grant of the monitoring waiver by the Superintendent (Section 6.4 B)

must be included as a condition in the User’s permit or other control

mechanism.

B.      Wastewater discharge permits may contain, but need not be limited to, the following

Conditions:

(1)     Limits on the average and/or maximum rate of discharge, time of discharge, and/or

requirements for flow regulation and equalization;

(2)     Requirements for the installation of pretreatment technology. pollution control, or

construction of appropriate containment devices, designed to reduce, eliminate, or prevent

the introduction of pollutants into the treatment works;

(3)      Requirements for the development and implementation of spill control plans or other

special conditions including management practices necessary to adequately prevent

accidental, unanticipated, or nonroutine discharges;

(4)      Development and implementation of waste minimization plans to reduce the amount of

pollutants discharged to the POTW;

(5)      The unit charge or schedule of user charges and fees for the management of the

wastewater discharged to the POTW;

(6)      Requirements for installation and maintenance of inspection and sampling facilities and

Equipment, including flow measurement devises;

(7)       A statement that compliance with the wastewater discharge permit does not relieve the

permittee of responsibility for compliance with all applicable Federal and State

pretreatment standards, including those which become effective during the term of the

wastewater discharge permit; and

(8)       Other conditions as deemed appropriate by the Superintendent to ensure compliance with

this ordinance, and State and Federal laws, rules, and regulations.

5.3	Wastewater Discharge Permit Appeals

The Superintendent shall provide public notice of the issuance of a wastewater discharge

permit. Any person, including the user, may petition the Superintendent to reconsider the terms

of a wastewater discharge permit within thirty (30) days of notice of its issuance. Public notice

shall consist of publication in a newspaper of general circulation in Crawford County, Illinois.

A.	Failure to submit a timely petition for review shall be deemed to be a waiver of the

administrative appeal.

B.	In its petition, the appealing party must indicate the wastewater discharge permit

provisions objected to, the reasons for this objection, and the alternative condition, if

any, it seeks to place in the wastewater discharge permit.

C.	The effectiveness of the wastewater discharge permit shall not be stayed pending the

appeal.

D.	If the Superintendent fails to act within thirty (30) days. a request for reconsideration

shall be deemed to be denied. Decisions of the Superintendent not to reconsider a

wastewater discharge permit, not to issue a wastewater discharge permit, or not to modify

a wastewater discharge permit may be appealed by the aggrieved party to the Wastewater

Treatment Committee of the City within 30 days after it becomes final. If the Wastewater

Treatment Committee of the City fails to act on the request within 60 days, a request for

reconsideration shall be deemed denied. The decisions of the Wastewater Treatment

Committee of the City may be appealed by the aggrieved party to the City Council within

thirty (30) days by the filing with the City Clerk of a request for reconsideration. If the

City Council fails to act on the request within thirty (30) days, a request for

reconsideration shall be deemed denied by the City Council. Decisions of the City

Council not to consider a request for reconsideration shall be considered final

administrative action for purposes of judicial review. The City Council’s decision on the

merits of the request for reconsideration shall be considered a final administrative action

for purposes of judicial review.

E.	Aggrieved parties seeking judicial review of the final administrative wastewater

discharge permit decision must do so by filing a complaint with the Circuit Court of the

Second Judicial District, Crawford County, Illinois, within thirty-five (35) days.

Review shall be in accordance with the Administrative Review Act, 735 ILCS 5/1 et

seq.

5.4	Wastewater Discharge Permit Modification

The Superintendent may modify a wastewater discharge permit for good cause, including, but not limited to, the following reasons:

A. To incorporate any new or revised Federal, State, or local pretreatment standards or

requirements;

B.  To address significant alterations or additions to the users 5 operation, processes, or

wastewater volume or character since the time of wastewater discharge permit

issuance;

C. A change in the POTW that requires either a temporary or permanent reduction or

elimination of the authorized discharge;

D. Information indicating that the permitted discharge poses a threat to the City's POTW,

City personnel, or the receiving waters;

E. Violation of any terms or conditions of the wastewater discharge permit;

F. Misrepresentations or failure to fully disclose all relevant facts in the wastewater

discharge permit application or in any required reporting;

G. Revision of or a grant of variance from categorical pretreatment standards pursuant to

40 CFR 403.13;

H. To correct typographical or other errors in the wastewater discharge permit; or

I. To reflect a transfer of the facility ownership or operation to a new owner or operator.

(Note: Modification for this purpose may not be allowed unless the permit is

transferable as provided in Section 5.5.)

5.5	Wastewater Discharge Permit Transfer

Wastewater discharge permits may be transferred to a new owner or operator only if the

permittee gives at least ninety (90) days advance notice to the Superintendent and the

Superintendent approves the wastewater discharge permit transfer.  The notice to the

Superintendent must include a written certification by the new owner or operator which:

A. States that the new owner and/or operator has no immediate intent to change the

facility's operations and processes;

B. Identifies the specific date on which the transfer is to occur; and

C. Acknowledges full responsibility for complying with the existing wastewater discharge

permit.

Failure to provide advance notice of a transfer renders the wastewater discharge permit void as of the date of facility transfer. For good cause shown, the Superintendent may shorten the advance notice requirements of this Section.

5.6	Wastewater Discharge Permit Revocation

The Superintendent may revoke a wastewater discharge permit for good cause, including,

but not limited to, the following reasons:

A. Failure to notify the Superintendent of significant changes to the wastewater prior to the

changed discharge;

B. Failure to provide prior notification to the Superintendent of changed conditions pursuant

to Section 6.5 of this ordinance;

C.	 Misrepresentation or failure to fully disclose all relevant facts in the wastewater

discharge permit application;

D. Falsifying self-monitoring reports;

E. Tampering with monitoring equipment:

F. Refusing to allow the Superintendent timely access to the facility premises and records;

G. Failure to meet effluent limitations;

H. Failure to pay fines;

I. Failure to pay sewer charges;

J.	Failure to meet compliance schedules;

K.	Failure to complete a wastewater survey or the wastewater discharge permit application;

L.	Failure to provide advance notice of the transfer of business ownership of a permitted

facility; or

M.	Violation of any pretreatment standard or requirement, or any terms of the wastewater

discharge permit or this ordinance.

Wastewater discharge permits shall be voidable upon cessation of operations or transfer of

business ownership. All wastewater discharge permits issued to a particular user are void upon

the issuance of a new wastewater discharge permit to that user.

A decision of the Superintendent to revoke a wastewater discharge permit may be appealed

to the Wastewater Treatment Committee of the City within 30 days after it becomes final. If the

Wastewater Treatment Committee of the City fails to act on the request within ten (10) days, the

appeal will be deemed to have been denied. The decision of the Wastewater Treatment

Committee of the City may be appealed by the aggrieved party to the City Council within thirty

(30) days by the filing with the City Clerk of a request for reconsideration. If the City Council

fails to act on the request within thirty (30) days, a request for reconsideration shall be deemed

denied by the City Council. Decisions of the City Council not to consider a request for

reconsideration shall be considered final administrative action for purposes of judicial review.

The City Councils S decision on the merits of the request for reconsideration shall be considered

a final administrative action for purposes of judicial review. Aggrieved parties seeking judicial

review of the final administrative decision must do so by filing a complaint with the Circuit

Court of the Second Judicial District, Crawford County, Illinois, within thirty-five (35) days

from the final administrative action. Review shall be in accordance with the Administrative

Review Act, 735 ILCS 5/1 et seq.

5.7	Wastewater Discharge Permit Reissuance

A user with an expiring wastewater discharge permit shall apply for wastewater discharge

permit reissuance by submitting a complete permit application, in accordance with Section 4.5 of

this ordinance, a minimum of one hundred eighty (180) days prior to the expiration of the user's

existing wastewater discharge permit. For good cause shown, the Superintendent may shorten the

advance notice requirements of this Section.

5.8	Regulation of Waste Received from Other Jurisdictions

A. If another municipality, or user located within another municipality, contributes wastewater

to the POTW, the City shall enter into an intermunicipal agreement with the contributing

municipality.

B. Prior to entering into an agreement required by paragraph A, above, the Superintendent shall

request the following information from the contributing municipality:

(1)  A description of the quality and volume of wastewater discharged to the POTW by the

contributing municipality;

(2)  An inventory of all users located within the contributing municipality that are discharging

to the POTW; and

(3)  Such other information as the Superintendent may deem necessary.

C. An intermunicipal agreement, as required by paragraph A, above, shall contain the

following conditions:

(1) A requirement for the contributing municipality to adopt a sewer use ordinance which is

at least as stringent as this ordinance and local limits which are at least as stringent as

those set out in Section 2.4 of this ordinance. The requirement shall specify that such

ordinance and limits must be revised as necessary to reflect changes made to the City's

ordinance or local limits;

(2) A requirement for the contributing municipality to submit a revised user inventory on at

least an annual basis;

(3) A provision specifying which pretreatment implementation activities, including

wastewater discharge Permit issuance, inspection and sampling, and enforcement, will

be conducted by the contributing municipality; which of these activities will be

conducted by the Superintendent; and which of these activities will be conducted jointly

by the contributing municipality and the Superintendent;

(4) A requirement for the contributing municipality to Superintendent with access to all

information that the contributing municipality as part of its pretreatment activities;

(5) Limits on the nature, quality, and volume of the contributing municipality's wastewater

at the point where it discharges to the POTW;

(6) Requirements for monitoring the contributing municipality's discharge;

(7) A provision ensuring the Superintendent access to the facilities of users located within

the contributing municipality's jurisdictional boundaries for the purpose of inspection,

sampling, and any other duties deemed necessary by the Superintendent; and

(8) A provision specifying remedies available for breach of the terms of the intermunicipal

agreement.

SECTION 6- REPORTING REQUIREMENTS

6.1	Baseline Monitoring Reports

A.	Within either one hundred eighty (180) days after the effective date of a categorical

pretreatment standard, or the final administrative decision on a category determination

under 40 CFR 403.6(a)(4), whichever is later, existing categorical users currently

discharging to or scheduled to discharge to die POTW shall submit to  the Superintendent

a report which contains The information listed in paragraph B, below. At least ninety (90)

days prior to commencement of their discharge, new sources, and sources that become

categorical users subsequent to the promulgation of an applicable categorical standard,

shall submit to the Superintendent a report which contains the information listed in

paragraph B, below. A new source shall report the method of pretreatment it intends to

use to meet applicable categorical standards. A new source also shall give estimates of its

anticipated flow and quantity of pollutants to be discharged.

B.	Users described above shall submit the information set forth below.

(1) Identifying Information. The name and address of the facility, including the name of

the operator and owner.

(2) Environmental Permits. A list of any environmental control permits held by or for the

facility.

(3) Description of Operations. A brief description of the nature, average rate of

production, and standard industrial classifications of the operation(s) carried out by

such user. This description should include a schematic process diagram which

indicates points of discharge to the POTW from the regulated processes.

(4) Flow Measurement. Information showing the measured average daily and maximum

daily flow, in gallons per day. to The POTW from regulated process streams and

other streams, as necessary, to allow use of the combined wastestream formula set

out in 40 CFR 403.6(e).

(5) Measurement of Pollutants.

(a)	The categorical pretreatment standards applicable to each regulated process.

(b) The results of sampling and analysis identifying the nature and concentration,

and/or mass, where required by the standard or by the Superintendent, of

regulated pollutants in the discharge from each regulated process. Instantaneous,

daily maximum, and long-term average concentrations, or mass, where required,

shall be reported. The sample shall be representative of daily operations and shall

be analyzed in accordance with procedures set out in Section 6.10 of this

ordinance.

(c)	Sampling must be performed in accordance with procedures set out in Section

6.11 of this ordinance.

(6) Certification.  A statement, reviewed by the user's authorized representative and

certified by a qualified professional, indicating whether pretreatment standards are

being met on a consistent basis. and, if not, whether additional operation and

maintenance (O&M) and/or additional pretreatment is required to meet the

pretreatment standards and requirements.

(7) Compliance Schedule. If additional pretreatment and/or O&M will be required to

meet the pretreatment standards, the shortest schedule by which the user will provide

such additional pretreatment and/or O&M. The completion date in this schedule shall

not be later than the compliance date established for the applicable pretreatment

standard.  A compliance schedule pursuant to this section must meet the

requirements set out in Section 6.2 of this ordinance.

(8) Signature and Certification.  All baseline monitoring reports must be signed and

certified in accordance with Section 4.6 of this ordinance.

6.2 Compliance Schedule Progress Reports

The following conditions shall apply to the compliance schedule required by Section

6. 1(B)(7) of this ordinance:

A.	 The schedule shall contain progress increments in the form of dates for the

commencement and completion of major events leading to the construction and

operation of additional pretreatment required for the user to meet the applicable

pretreatment standards (such events include, but are not limited to, hiring an engineer,

completing preliminary and final plans, executing contracts for major components,

commencing and completing construction, and beginning and conducting routine

operation);

B. No increment referred to above shall exceed nine (9) months;

C. The user shall submit a progress report to the Superintendent no later than fourteen (14)

days following each date in the schedule and the final date of compliance including, as

a minimum, whether or not it complied with the increment of progress, the reason for

any delay, and, if appropriate, the steps being taken by the user to return to the

established schedule; and

D. In no event shall more than nine (9) months elapse between such progress reports to the

Superintendent.

6.3 Reports on Compliance with Categorical Pretreatment Standard Deadline

Within ninety (90) days following the date for final compliance with applicable categorical

pretreatment standards, or in the case of a new source following commencement of the

introduction of wastewater into the POTW, any user subject to such pretreatment standards and

requirements shall submit to the Superintendent a report containing the information described in

Section 6.1 (B)(4-6) of this ordinance. For users subject to equivalent mass or concentration

limits established in accordance with the procedures in 40 CFR 403.6(c), this report shall contain

a reasonable measure of the user’s long-term production rate. For all other users subject to

categorical pretreatment standards expressed in terms of allowable pollutant discharge per unit of

production (or other measure of operation), this report shall include the user's actual production

during the appropriate sampling period. All compliance reports must be signed and certified in

accordance with Section 4.6 of this ordinance.

6.4 Periodic Compliance Reports

A. Except as specified in Section 6.4.C, all Significant Industrial Users must, at a frequency

determined by the Superintendent submit no less than twice per year (June and December)

reports indicating the nature, concentration of pollutants in the discharge which are limited

by Pretreatment Standards and the measured or estimated average and maximum daily

flows for the reporting period.  In cases where the Pretreatment Standard requires

compliance with a Best Management Practice (BMP) or pollution prevention alternative,

the User must submit documentation required by [the Superintendent] or the Pretreatment

Standard necessary to determine the compliance status of the User.

B. The City may authorize an Industrial User subject to a categorical Pretreatment Standard to

forego sampling of a pollutant regulated by a categorical Pretreatment Standard if the

Industrial User has demonstrated through sampling and other technical factors that the

pollutant is neither present nor expected to be present in the Discharge, or is present only at

background levels from intake water and without any increase in the pollutant due to

activities of the Industrial User. [see 40 CFR 403.12(e)(2)] This authorization is subject to

the following conditions:

        - The waiver may be authorized where a pollutant is determined to be present solely due to sanitary wastewater discharged from the facility provided that the sanitary wastewater is not regulated by an applicable categorical Standard and otherwise includes no process wastewater.

        - The monitoring waiver is valid only for the duration of the effective period of the individual wastewater discharge permit, but in no case longer than 5 years.  The User must submit a new request for the waiver before the waiver can be granted for each subsequent individual wastewater discharge permit. See Section 4.5A(8).

        - In making a demonstration that a pollutant is not present, the Industrial User must provide data from at least one sampling of the facility’s process wastewater prior to any treatment present at the facility that is representative of all wastewater from all processes.

        - The request for a monitoring waiver must be signed in accordance with Section 1.4C, and include the certification statement in 6.14 A (40 CFR 403.6(a)(2)(ii)).

        - Non-detectable sample results may be used only as a demonstration that a pollutant is not present if the EPA approved method from 40 CFR Part 136 with the lowest minimum detection level for that pollutant was used in the analysis.

        - Any grant of the monitoring waiver by the Superintendent must be included as a condition in the User’s permit. The reasons supporting the waiver and any information submitted by the User in its request for the waiver must be maintained by the Superintendent for 3 years after expiration of the waiver.

        - Upon approval of the monitoring waiver and revision of the User’s permit by the Superintendent, the Industrial User must certify on each report with the statement in Section 6.14 C below, that there has been no increase in the pollutant in its wastestream due to activities of the Industrial User.

(8) In the event that a waived pollutant is found to be present or is expected to be present because of changes that occur in the User’s operations, the User must immediately: Comply with the monitoring requirements of Section 6.4 A, or other more frequent monitoring requirements imposed by the Superintendent, and notify the Superintendent.

(9) This provision does not supersede certification processes and requirements established in categorical Pretreatment Standards, except as otherwise specified in the categorical Pretreatment Standard.

C.    All wastewater samples must be representative of the User’s discharge.  Wastewater

monitoring and flow measurement facilities shall be properly operated, kept clean, and

maintained in good working order at all times.  The failure of a User to keep its monitoring

facility in good working order shall not be grounds for the User to claim that sample results

are unrepresentative of its discharge.

D.    If a user subject to the reporting requirement in this section monitors any pollutant more

frequently than required by the Superintendent, using the procedures prescribed in Section

6.11 of this ordinance, the results of this monitoring shall be included in the report.

E.    All periodic compliance reports must be signed and certified in accordance with section 6.14

A of this ordinance.

6.5	Reports of Changed Conditions

Each user must notify the Superintendent of any planned significant changes to the user's

operations or system which might alter the nature, quality, or volume of its wastewater at least

ninety (90) days before the change.

A.	 The Superintendent may require the User to submit such information as may be deemed

necessary to evaluate the changed condition, including the submission of a wastewater

discharge permit application under Section 4.5 of this ordinance.

B. The Superintendent may issue a wastewater discharge permit under Section 4.7 of this

ordinance or modify an existing wastewater discharge permit under Section 5.4 of tins

ordinance in response to changed conditions or anticipated changed conditions

C. For purposes of this requirement, significant changes include, but are not limited to, flow

increases of twenty percent (20%) or greater, and the discharge of any previously

unreported pollutants.

6.6	Reports of Potential Problems

A. In case of any discharge, including, but not limited to, accidental discharges. discharges

of a nonroutine, episodic nature, a noncustomary batch discharge, or a slug load, that

may cause potential problems for the POTW, the user shall immediately telephone and

notify the Superintendent of the incident. The user shall contact the Superintendent or

POTW operators at (618) 544-8110 or, (618) 544-8476 between 7 a.m. and 4 p.m.,

Monday through Thursday, and 6 a.m. and 2 p.m. on Friday, and between 8 a.m. and

noon on Saturday and Sunday, and at all other times, through the Robinson Fire

Department at (618) 544-2955. This notification shall include the location of the

discharge, type of waste, concentration and volume, if known, and corrective actions

taken by the user.

B. Within five (5) days following such discharge, the user shall, unless waived by the

Superintendent, submit a detailed written report describing the cause(s) of the discharge

and the measures to be taken by the user to prevent similar future occurrences. Such

notification shall not relieve the user of any expense, loss, damage, or other liability

which may be incurred as a result of damage to the POTW, natural resources, or any

other damage to person or property; nor shall such notification relieve the user of any

fines, penalties, or other liability which may be imposed pursuant to this ordinance.

C. A notice shall be permanently posted on the user's bulletin board or other prominent

place advising employees whom to call in the event of a discharge described in paragraph

A, above. Employers shall ensure that all employees, who may cause such a discharge to

occur, are advised of the emergency notification procedure.

D. Significant Industrial Users are required to notify the Superintendent immediately of

any changes at its facility affecting the potential for a Slug Discharge.

6.7	Reports from Unpermitted Users

All users not required to obtain a wastewater discharge permit shall provide appropriate

reports to the Superintendent as the Superintendent may require.

6.8	Notice of Violation/Repeat Sampling and Reporting

If sampling performed by a user indicates a violation, the user must notify the

Superintendent within twenty-four (24) hours of becoming aware of the violation. The user shall

also repeat the sampling and analysis and submit the results of the repeat analysis to the

Superintendent within thirty (30) days after becoming aware of the violation. The user is not

required to resample if the Superintendent monitors at the user's facility at least once a month, or

if the Superintendent samples between the user’s initial sampling and when the user receives the

results of this sampling.

6.9       Notification of the Discharge of Hazardous Waste

The discharge of any material classified as hazardous waste as set forth in 40 CFR part 261

is strictly and expressly prohibited.

In the event of accidental discharges,  the IU shall notify the POTW, the EPA Regional Waste Management Division Director, and State hazardous waste authorities, in writing, of any discharge into the POTW of a substance which, if otherwise disposed of, would be a hazardous waste under 40 CFR Part 261.  Such notification must include the name of the hazardous waste as set forth in 40 CFR Part 261, the EPA hazardous waste number, and the type of discharge (continuous, batch, or other).  If the User discharges more than one hundred (100) kilograms of such waste per calendar month to the POTW, the notification also shall contain the following information to the extent such information is known and readily available to the User:  an identification of the hazardous constituents contained in the wastes, an estimation of the mass and concentration of such constituents in the wastestream discharged during that calendar month, and an estimation of the mass of constituents in the wastestream expected to be discharged during the following twelve (12) months.  All notifications must take place no later than one hundred and eighty (180) days after the discharge commences.  Any notification under this paragraph need be submitted only once for each hazardous waste discharged.  However, notifications of changed conditions must be submitted under Section 6.5 of this ordinance.  The notification requirement in this Section does not apply to pollutants already reported by Users subject to categorical Pretreatment Standards under the self-monitoring requirements of Sections 6.1, 6.3, and 6.4 of this ordinance.

6.10	Analytical Requirements

All pollutant analyses, including sampling techniques, to be submitted as part of a

wastewater discharge permit application or report shall be performed using validated analytical methods or any other sampling and analytical procedures, including procedures suggested by the POTW or other parties, approved by the Administrator in accordance with the techniques prescribed in 40 CFR Part 136, unless otherwise specified in an applicable categorical

pretreatment standard. If 40 CFR Part 136 does not contain sampling or analytical techniques for

the pollutant in question, sampling and analyses must be performed in accordance with

procedures approved by USEPA.

6.11	Sample Collection

A.  Except as indicated in Section B and C below, the User must collect wastewater samples

using 24-hour flow-proportional composite sampling techniques, unless

time-proportional composite sampling or grab sampling is authorized by the

Superintendent.  Where time-proportional composite sampling or grab sampling is

authorized by the City, the samples must be representative of the discharge.  Using

protocols (including appropriate preservation) specified in 40 CFR Part 136 and

appropriate EPA guidance, multiple grab samples collected during a 24-hour period may

be composited prior to the analysis as follows: for cyanide, total phenols, and sulfides the

samples may be composited in the laboratory or in the field; for volatile organics and oil

and grease, the samples may be composited in the laboratory. Composite samples for

other parameters unaffected by the compositing procedures as documented in approved

EPA methodologies may be authorized by the City, as appropriate. In addition, grab

samples may be required to show compliance with Instantaneous Limits.

B. Samples for oil and grease, temperature, pH, cyanide, phenols, sulfides, and volatile

organic compounds must be obtained using grab collection techniques.

C. For sampling required in support of baseline monitoring and 90-day compliance reports

required in Section 6.1 and 6.3 [40 CFR 403.12(b) and (d)], a minimum of four (4) grab

samples must be used for pH, cyanide, total phenols, oil and grease, sulfide and volatile

organic compounds for facilities for which historical sampling data do not exist; for

facilities for which historical sampling data are available, the Superintendent may

authorize a lower minimum.

For the reports required by paragraphs Section 6.4 (40 CFR 403.12(e) and 403.12(h)), the

Industrial User is required to collect the number of grab samples necessary to assess and

assure compliance by with applicable Pretreatment Standards and Requirements.

6.12      Timing

Written reports will be deemed to have been submitted on the date postmarked. For reports

which are not mailed, postage prepaid, into a mail facility serviced by the United States Postal

Service, the date of receipt of the report shall govern.

6.13	Record Keeping

Users subject to the reporting requirements of this ordinance shall retain, and make

available for inspection and copying, all records of information obtained pursuant to any

monitoring activities required by this ordinance, any additional records of information

obtained pursuant to monitoring activities undertaken by the User independent of such

requirements, and documentation associated with Best Management Practices established

under Section 2.4 C.  Records shall include the date, exact place, method, and time of

sampling, and the name of the person(s) taking the samples; the dates analyses were

performed; who performed the analyses; the analytical techniques or methods used; and the

results of such analyses.  These records shall remain available for a period of at least three

(3) years.  This period shall be automatically extended for the duration of any litigation

concerning the User or the City, or where the User has been specifically notified of a longer

retention period by the Superintendent.

6.14	Certification Statements

- Certification of Permit Applications, User Reports and Initial Monitoring Waiver. The following certification statement is required to be signed and submitted by Users submitting permit applications in accordance with Section 4.7; Users submitting baseline monitoring reports under Section 6.1 B (5) [Note: See 40 CFR 403.12 (l)]; Users submitting reports on compliance with the categorical Pretreatment Standard deadlines under Section 6.3 [Note: See 40 CFR 403.12(d)]; Users submitting periodic compliance reports required by Section 6.4 A–D [Note: See 40 CFR 403.12(e) and (h)], and Users submitting an initial request to forego sampling of a pollutant on the basis of Section  6.4B(4)[Note: See 40 CFR 403.12(e)(2)(iii)]. The following certification statement must be signed by an Authorized Representative as defined in Section 1.4 C:

I certify under penalty of law that this document and all attachments were prepared under my direction or supervision in accordance with a system designed to assure that qualified personnel properly gather and evaluate the information submitted.  Based on my inquiry of the person or persons who manage the system, or those persons directly responsible for gathering the information, the information submitted is, to the best of my knowledge and belief, true, accurate, and complete.  I am aware that there are significant penalties for submitting false information, including the possibility of fine and imprisonment for knowing violations.

B.   Annual Certification for Non-Significant Categorical Industrial Users—A  facility determined to be a Non-Significant Categorical Industrial User by the Superintendent pursuant to 1.4 GG(3)  and 4.7 C [Note: See 40 CFR 403.3(v)(2)] must annually submit the following certification statement signed in accordance with the signatory requirements in 1.4 C [Note: See 40 CFR 403.120(l)].  This certification must accompany an alternative report required by the Superintendent:

Based on my inquiry of the person or persons directly responsible for managing compliance with the categorical Pretreatment Standards under 40 CFR ____, I certify that, to the best of my knowledge and belief that during the period from __________, ________ to ________, ________ [months, days, year]:

(a) The facility described as ____________________

[facility name] met the definition of a Non-Significant Categorical Industrial User as described in 1.4 GG (3); [Note: See 40 CFR 403.3(v)(2)]

(b) The facility complied with all applicable Pretreatment Standards and requirements during this reporting period; and (c) the facility never discharged more than 100 gallons of total categorical wastewater on any given day during this reporting period.

This compliance certification is based on the following information.

________________________________________________

________________________________________________

C.	Certification of Pollutants Not Present

Users that have an approved monitoring waiver based on Section 6.4 B must certify on each report with the following statement that there has been no increase in the pollutant in its wastestream due to activities of the User. [Note: See 40 CFR 403.12(e)(2)(v)]

Based on my inquiry of the person or persons directly responsible for managing compliance with the Pretreatment Standard for 40 CFR _______ [specify applicable National Pretreatment Standard part(s)], I certify that, to the best of my knowledge and belief, there has been no increase in the level of ______ [list pollutant(s)] in the wastewaters due to the activities at the facility since filing of the last periodic report under Section 6.4.A.

SECTION 7- COMPLIANCE MONITORING

7.1	Right of Entry: Inspection and Sampling

The Superintendent shall have the right to enter the premises of any user to determine

whether the user is complying with all requirements of this ordinance and any wastewater

discharge permit or order issued hereunder. Users shall allow the Superintendent ready access to

all parts of the premises for the purposes of inspection, sampling, records examination and

copying, and the performance of any additional duties.

A. Where a user has security measures in force which require proper identification and

clearance before entry into its premises, the user shall make necessary arrangements with

its security guards so that, upon presentation of suitable identification,  the

Superintendent will be permitted to enter without delay for the purposes of performing

specific responsibilities.

B. The Superintendent shall have the right to set up on the user's property, or require

installation of, such devices as are necessary to conduct sampling and/or metering of the

user's operations.

C. The Superintendent may require the user to install monitoring equipment as necessary.

The facility's sampling and monitoring equipment shall be maintained at all times in a

safe and proper operating condition by the user at its own expense. All devices used to

measure wastewater flow and quality shall be calibrated every 6 months (unless

otherwise specified in a Wastewater Discharge permit) to ensure their accuracy.

D. Any temporary or permanent obstruction to safe and easy access to the facility to he

inspected and/or sampled shall be promptly removed by the user at the written or verbal

request of the Superintendent and shall not be replaced. The costs of clearing such access

shall be born by the user

E.	Unreasonable delays in allowing the Superintendent access to the user’s premises shall be

a violation of this ordinance.

7.2	Search Warrants

If the Superintendent has been refused access to a building, structure, or property, or any

part thereof, and is able to demonstrate probable cause to believe that there may be a violation of

this ordinance, or that there is a need to inspect and/or sample as part of a routine inspection and

sampling program of the City designed to verify compliance with this ordinance or any permit or

order issued hereunder, or to protect the overall public health, safety and welfare of the

community, then the Superintendent may seek issuance of a search warrant from the Circuit

Court of the Second Judicial District, Crawford County, Illinois.

SECTION 8- CONFIDENTIAL INFORMATION

Information and data on a user obtained from reports, surveys, wastewater discharge permit

applications, wastewater discharge permits, and monitoring programs, and from the

Superintendent's inspection and sampling activities, shall be available to the public without

restriction, unless the user specifically requests, and is able to demonstrate to the satisfaction of

the Superintendent, that the release of such information would divulge information, processes, or

methods of production entitled to protection as trade secrets under applicable State law. Any

such request must be asserted at the time of submission of the information or data. When

requested and demonstrated by the user furnishing a report that such information should be held

confidential, the portions of a report which might disclose trade secrets or secret processes shall

not be made available for inspection by the public, but shall be made available immediately upon

request to governmental agencies for uses related to the NPDES program or pretreatment

program, and in enforcement proceedings involving the person furnishing the report. Wastewater

constituents and characteristics and other “effluent data” as defined by 40 CFR 2.302 will not be

recognized as confidential information and will be available to the public without restriction.

SECTION 9 - PUBLICATION OF USERS IN SIGNIFICANT NONCOMPLIANCE

The Superintendent shall publish annually, in a newspaper of general circulation that provides meaningful public notice within the jurisdictions served by the City of Robinson, a list of the Users which, at any time during the previous twelve (12) months, were in Significant Noncompliance with applicable Pretreatment Standards and Requirements.  The term Significant Noncompliance shall be applicable to all Significant Industrial Users (or any other Industrial User that violates paragraphs (C), (D) or (H) of this Section) and shall mean:

A.  Chronic violations of wastewater discharge limits, defined here as those in which sixty-six percent (66%) or more of all the measurements taken for the same pollutant parameter taken during a six (6) month period exceed (by any magnitude) a numeric Pretreatment Standard or Requirement, including Instantaneous Limits as defined in Section 2;

B.   Technical Review Criteria (TRC) violations, defined here as those in which thirty-three percent (33%) or more of wastewater measurements taken for each pollutant parameter during a six (6) month period equals or exceeds the product of the numeric Pretreatment Standard or Requirement including Instantaneous Limits, as defined by Section 2 multiplied by the applicable criteria (1.4 for BOD, TSS, fats, oils and grease, and 1.2 for all other pollutants except pH);

C.  Any other violation of a Pretreatment Standard or Requirement as defined by Section 2 (Daily Maximum, long-term average, Instantaneous Limit, or narrative standard) that the Superintendent determines has caused, alone or in combination with other discharges, Interference or Pass Through, including endangering the health of POTW personnel or the general public;

D. Any discharge of pollutants that has caused imminent endangerment to the public or to

the environment, or has resulted in the Superintendent's exercise of its emergency

authority to halt or prevent such a discharge;

E. Failure to meet, within ninety (90) days of the scheduled date, a compliance schedule

milestone contained in a wastewater discharge permit or enforcement order for starting

construction, completing construction, or attaining final compliance;

F. Failure to provide within thirty (30) days after the due date, any required reports,

including baseline monitoring reports, reports on compliance with categorical

pretreatment standard deadlines, periodic self-monitoring reports, and reports on

compliance with compliance schedules;

G. Failure to accurately report noncompliance; or

H. Any other violation(s), which may include a violation of Best Management Practices, which the Superintendent determines will adversely affect the operation or implementation of the local pretreatment program.

SECTION 10 - ADMINISTRATIVE ENFORCEMENT REMEDIES

10.1	Notification of Violation

When the Superintendent finds that a user has violated, or continues to violate, any

provision of this ordinance, a wastewater discharge permit or order issued hereunder, or any

other pretreatment standard or requirement, the Superintendent may serve upon that user a

written Notice of Violation. Within thirty (30) days of the receipt of this notice, an explanation of

the violation and a plan for the satisfactory correction and prevention thereof, to include specific

required actions, shall be submitted by the user to the Superintendent. Submission of this plan in

no way relieves the user of liability for any violations occurring before or after receipt of the

Notice of Violation Nothing in this section shall limit the authority of the Superintendent to take

any action, including emergency actions or any other enforcement action, without first issuing a

Notice of Violation.

10.2	Consent Orders

The Superintendent may enter into Consent Orders, assurances of voluntary compliance, or

other similar documents establishing an agreement with any user responsible for noncompliance.

Such documents will include specific action to be taken by the user to correct the noncompliance

within a time period specified by the document. Such documents shall have the same force and

effect as the administrative orders issued pursuant to Sections 10.4 and 10.5 of this ordinance

and shall be judicially enforceable.

10.3	Show Cause Hearing

The Superintendent may order a user which has violated, or continues to violate, any

provision of this ordinance, a wastewater discharge permit or order issued hereunder, or any

other pretreatment standard or requirement, to appear before the Superintendent and show cause

why the proposed enforcement action should not be taken. Notice shall be served on the user

specifying the time and place for the meeting, the proposed enforcement action, the reasons for

such action, and a request that the user show cause why the proposed enforcement action should

not be taken. The notice of the meeting shall be served personally or by registered or certified

mail (return receipt requested) at least thirty (30) days prior to the hearing. Such notice may be

served on any authorized representative of the user. A show cause bearing shall not be a bar

against, or prerequisite for, taking any other action against the user.

10.4	Compliance Orders

When the Superintendent finds that a user has violated, or continues to violate, any

provision of this ordinance, a wastewater discharge permit or order issued hereunder, or any

other pretreatment standard or requirement, the Superintendent may issue an order to the user

responsible for the discharge directing that the user come into compliance within a specified

time. If the user does not come into compliance within the time provided, sewer service may be

discontinued unless adequate treatment facilities4 devices, or other related appurtenances are

installed and properly operated. Compliance orders also may contain other requirements to

address the noncompliance, including additional self-monitoring and management practices

designed to minimize the amount of pollutants discharged to the sewer. A compliance order may

not extend the deadline for compliance established for a pretreatment standard or requirement,

nor does a compliance order relieve the user of liability for any violation, including any

continuing violation. Issuance of a compliance order shall flat be a bar against, or a prerequisite

for, taking any other action against the user.

10.5	Cease and Desist Orders

When the Superintendent finds that a user has violated, or continues to violate, any

provision of this ordinance, a wastewater discharge permit or order issued hereunder, or any

other pretreatment standard or requirement, or that the user's past violations are likely to recur,

the Superintendent may issue an order to the user directing it to cease and desist all such

violations and directing the user to:

A. Immediately comply with all requirements: and

B. Take such appropriate remedial or preventive action as may be needed to properly

address a continuing or threatened violation, including halting operations and/or

terminating the discharge.

Issuance of a cease and desist order shall not be a bar against, or a prerequisite for, taking any

other action against the user.

10.6	Administrative Fines

A.  When the Superintendent] finds that a user has violated, or continues to violate, any

provision of this ordinance, a wastewater discharge permit or order issued hereunder,

or any other pretreatment standard or requirement, the Superintendent may fine such

user in an amount not to exceed $ 1,000.00 dollars. Such fines shall be assessed on a

per violation, per day basis. In the case of monthly or other long term average

discharge limits, fines shall be assessed for each day during the period of violation.

B. Unpaid charges, fines, and penalties shall, after thirty (30) calendar days, be assessed

an additional penalty of Ten percent (10%) of the unpaid balance, and interest tall

accrue thereafter at a rate of ten percent (10%) per month. A lien against the user's

property will he sought for unpaid charges, fines, and penalties.

C. Users desiring to dispute such fines must file a written request for the Superintendent

to reconsider the fine along with full payment of the fine amount within thirty (30)

days of being notified of the fine. Where a request has merit, the Superintendent may

convene a hearing on the matter. In the event the user's appeal is successful, the

payment, together with any interest accruing thereto, shall be returned to the user. The

Superintendent may add the costs of preparing administrative enforcement actions,

such as notices and orders, to the fine.

D. Issuance of an administrative fine shall not be a bar against, or a prerequisite for,

taking any other action against the user.

10.7	Emergency Suspensions

The Superintendent may immediately suspend a user's discharge, after informal notice to

the user, whenever such suspension is necessary to stop an actual or threatened discharge which

reasonably appears to present or cause an imminent or substantial endangerment to the health or

welfare of persons. The Superintendent may also immediately suspend a user's discharge, after

notice and no more than 24 hours opportunity to respond, that threatens to interfere with the

operation of the POTW, or which presents, or may present, an endangerment to the environment.

A. Any user notified of a suspension of its discharge shall immediately stop or eliminate its

contribution. In the event of a user's failure to immediately comply voluntarily with

the suspension order, the Superintendent may take such steps as deemed necessary,

including immediate severance of the sewer connection, to prevent or minimize damage

to the POTW, its receiving stream, or endangerment to any individuals. The

Superintendent may allow the user to recommence its discharge when the user has

demonstrated to the satisfaction of the Superintendent that the period of endangerment

has passed, unless the termination proceedings in Section 10.8 of this ordinance are

initiated against the user.

B. A user that is responsible, in whole or in part, for any discharge presenting imminent

endangerment shall submit a detailed written statement, describing the causes of the

harmful contribution and the measures taken to prevent any future occurrence, to the

Superintendent prior to the date of any show cause or termination hearing under Sections

10.3 or 10.8 of this ordinance.

Nothing in this section shall be interpreted as requiring a hearing prior to any emergency

suspension under this section.

10.8	Termination of Discharge

In addition to the provisions in Section 5.6 of this ordinance, any user who violates the following conditions is subject to discharge termination:

A. Violation of wastewater discharge permit conditions:

B. Failure to accurately report the wastewater constituents and characteristics of its

discharge;

C. Failure to report significant changes in operations or wastewater volume, constituents,

and characteristics prior to discharge;

D. Refusal of reasonable access to the user’s premises for the purpose of inspection,

monitoring, or sampling; or

E. Violation of the pretreatment standards in Section 2 of this ordinance.

Such user will be notified of the proposed termination of its discharge and be offered an

opportunity to show cause under Section 10.3 of this ordinance why the proposed action should

not be taken. Exercise of this option by the Superintendent shall not be a bar to, or a prerequisite

for, taking any other action against the user

10.9	Review

A user may have review of the enforcement remedies and orders imposed by the

Superintendent, under Section 10. An appeal shall not stay the enforcement remedies and orders.

Decisions of the Superintendent under Section 10 may be appealed to the Wastewater

Treatment Committee of the City within 30 days after it becomes final. If the Wastewater

Treatment Committee of the City fails to act on the request within ten (10) days, the appeal will

be deemed to have been denied. The decision of the Wastewater Treatment Committee of the

City may be appealed by the aggrieved party to the City Council within thirty (30) days by the

filing with the City Clerk of a request for reconsideration. If the City Council fails to act on the

request within thirty (30) days, a request for reconsideration shall be deemed denied by the City

Council. Decisions of the City Council not to consider a request for reconsideration shall be

considered final administrative action for purposes of judicial review. The City Council's

decision on the merits of the request for reconsideration shall be considered a final administrative

action for purposes of judicial review. Aggrieved parties seeking judicial review of the final

administrative decision must do so by filing a complaint with the Circuit Court of the Second

Judicial District, Crawford County, Illinois, within thirty-five (35) days from the final

administrative action. Review shall be in accordance with the Administrative Review Act,

735 ILCS 511 et seq.

SECTION 11 - JUDICIAL ENFORCEMENT REMEDIES

11.1	Injunctive Relief

When the Superintendent finds that a user has violated, or continues to violate, any

provision of this ordinance, a wastewater discharge permit, or order issued hereunder, or any

other pretreatment standard or requirement, the Superintendent may petition the Circuit Court of

the Second Judicial District, Crawford County, Illinois, through the City's Attorney for the

issuance of a temporary or permanent injunction, as appropriate, which restrains or compels the

specific performance of the wastewater discharge permit, order, or other requirement imposed by

this ordinance on activities of the user. The Superintendent may also seek such other action as is

appropriate for legal and/or equitable relief, including a requirement for the user to conduct

environmental remediation. A petition for injunctive relief shall not be a bar against, or a

prerequisite for, taking any other action against a user.

11.2	Civil Penalties

A.	 A user who has violated, or continues to violate, any provision of this ordinance, a

wastewater discharge permit, or order issued hereunder, or any other pretreatment

standard or requirement shall be liable to the City for a maximum civil penalty of not

less than $1,000.00 dollars per violation, per day. In the case of a monthly or other long-

term average discharge limit, penalties shall accrue for each day during the period of the

violation.

B. The Superintendent may recover reasonable attorneys' fees, court costs, and other

expenses associated with enforcement activities, including sampling and monitoring

expenses, and the cost of any actual damages incurred by the City.

C. In determining the amount of civil liability, the Court shall take into account all relevant

circumstances, including, but not limited to, the extent of harm caused by the violation,

the magnitude and duration of the violation, any economic benefit gained through the

user's violation, corrective actions by the user, the compliance history of the user, and

any other factor as justice requires.

D. Filing a suit for civil penalties shall not be a bar against, or a prerequisite for, taking any

other action against a user.

11.3      Criminal Prosecution

A. A user who willfully or negligently violates any provision of this ordinance, a

wastewater discharge permit, or order issued hereunder, or any other pretreatment

standard or requirement shall, upon conviction, be guilty of a misdemeanor, punishable

by a fine of not more than $ 1,000.00 dollars per violation, per day, or imprisonment for

not more than one (1) year, or both.

B. A user who willfully or negligently introduces any substance into the POTW which

causes personal injury or property damage shall, upon conviction, be guilty of a

misdemeanor and be subject to a penalty of at least $ 1,000.00 dollars, or be subject to

imprisonment for not more than one (1) year, or both. This penalty shall be in addition to

any other cause of action for personal injury or property damage available under State

law.

C.	 A user who knowingly makes any false statements, representations, or certifications in

any application, record, report, plan, or other documentation filed, or required to be

maintained, pursuant to this ordinance, wastewater discharge permit, or order issued

hereunder, or who falsifies, tampers with, or knowingly renders inaccurate any

monitoring device or method required under this ordinance shall, upon conviction, be

punished by a fine of not more than $ 1,000.00 dollars per violation, per day, or

imprisonment for not more than one (1) year, or both.

D. In the event of a second conviction, a user shall be punished by a fine of not more than

$ 1,000.00 dollars per violation, per day, or imprisonment for not more than one (1) year,

or both.

11.4	Remedies Nonexclusive

The remedies provided for in this ordinance are not exclusive. The Superintendent

may take any, all, or any combination of these actions against a noncompliant user. Enforcement

of pretreatment violations will generally be in accordance with the City’s enforcement response

plan.  However, the Superintendent may take other action against any user when the

circumstances warrant.  Further, the Superintendent is empowered to take more than one

enforcement action against any noncompliant user.

SECTION 12- SUPPLEMENTAL ENFORCEMENT ACTION

12.1	Performance Bonds

The Superintendent may decline to issue or reissue a wastewater discharge permit to any

user who has failed to comply with any provision of this ordinance, a previous wastewater

discharge permit, or order issued hereunder, or any other pretreatment standard or requirement,

unless such user first files a satisfactory bond, payable to the City, in a sum not to exceed a value

determined by the Superintendent to be necessary to achieve consistent compliance.

12.2	Liability Insurance

The Superintendent may decline to issue or reissue a wastewater discharge permit to any

user who has tailed to comply with any provision of this ordinance, a previous wastewater

discharge permit, or order issued hereunder, or any other pretreatment standard or requirement,

unless the user first submits proof that it has obtained financial assurances sufficient to restore or

repair damage to the P0TW caused by its discharge.

12.3	Public Nuisances

A violation of any provision of this ordinance, a wastewater discharge permit, or order

issued hereunder, or any other pretreatment standard or requirement is hereby declared a public

nuisance and shall be corrected or abated as directed by the Superintendent. Any person(s)

creating a public nuisance shall be subject to the provisions of Robinson City Code, Chapter 12,

as amended, governing such nuisances, including reimbursing the City for any costs incurred in

removing, abating, or remedying said nuisance.

12.4	Contractor Listing

Users which have not achieved compliance with applicable pretreatment standards and

requirements are not eligible to receive a contractual award for the sale of goods or services to

the City. Existing contracts for the sale of goods or services to the City held by a user found to be

in significant noncompliance with pretreatment standards or requirements may be terminated at

the discretion of the Superintendent.

12.5 	Water Supply Severance

Whenever a User has violated or continues to violate any provision of this ordinance, an individual wastewater discharge permit, or non payment of sewer use charges, or order issued hereunder, or any other Pretreatment Standard or Requirement, water service to the User may be severed.  Service will recommence, at the User’s expense, only after the User has satisfactorily demonstrated its ability to comply.

SECTION 13 - AFFIRMATIVE DEFENSES TO DISCHARGE VIOLATIONS

13.1	Upset

A. For the purposes of this section, "upset” means an exceptional incident in which there is

unintentional and temporary noncompliance with categorical pretreatment standards

because of factors beyond the reasonable control of the user. An upset does not include

noncompliance to the extent caused by operational error, improperly designed treatment

facilities, inadequate treatment facilities, lack of preventive maintenance, or careless or

improper operation.

B. An upset shall constitute an affirmative defense to an action brought for

noncompliance with categorical pretreatment standards if the requirements of paragraph

(C), below, are met.

C. A user who wishes to establish the affirmative defense of upset shall demonstrate,

through properly signed, contemporaneous operating logs, or other relevant evidence

that:

(1)	An upset occurred and the user can identify the cause(s) of the upset,

(2)       The facility was at the time being operated in a prudent and workman-like manner

and in compliance with applicable operation and maintenance procedures; and

(3)       The user has submitted the following information to the Superintendent within

twenty-four (24) hours of becoming aware of the upset if this information is

provided orally, a written submission must be provided within five (5) days:

(a) A description of the indirect discharge and cause of noncompliance;

(b) The period of noncompliance, including exact dates and times or, if not

corrected, the anticipated time the noncompliance is expected to continue; and

(c) Steps being taken and/or planned to reduce, eliminate, and prevent recurrence

of the noncompliance.

D.	 In any enforcement proceeding, the user seeking to establish the occurrence of an upset

shall have the burden of proof.

E.	Users will have the opportunity for a judicial determination on any claim of upset only in

an enforcement action brought for noncompliance with categorical pretreatment

standards.

F.	Users shall control production of all discharges to the extent necessary to maintain

compliance with categorical pretreatment standards upon reduction, loss, or failure of its

treatment facility until the facility is restored or an alternative method of treatment is

provided. This requirement applies in the situation where, among other things, the

primary source of power of the treatment facility is reduced, lost, or fails.

13.2	Prohibited Discharge Standards

A user shall have an affirmative defense to an enforcement action brought against it for

noncompliance with the general prohibitions in Section 2.1(A) of this ordinance or the specific

prohibitions in Sections 2.l (B)(3) through (18) of this ordinance if it can prove that it did not

know, or have reason to know, that its discharge, alone or in conjunction with discharges from

other sources, would cause pass through or interference and that either:

A. A local limit exists for each pollutant discharged and the user was in compliance with

each limit directly prior to, and during, the pass through or interference: or

B. No local limit exists, but the discharge did not change substantially in nature or

constituents from the user s prior discharge when the City was regularly in compliance

with its NPDES permit and in the case of interference, was in compliance with

applicable sludge use or disposal requirements.

13.3	Bypass

A.	 For the purposes of this section,

(1)  “Bypass" means the intentional diversion of wastestreams from any portion of a

user's treatment facility.

(2) “Severe property damage” means substantial physical damage to property,

damage to the treatment facilities which causes them to become inoperable, or

substantial and permanent loss of natural resources which can reasonably be expected

to occur in the absence of a bypass.  Severe property damage does not mean

economic loss caused by delays in production.

B.	 A user may allow any bypass to Occur which does not cause pretreatment standards or

requirements to be violated but only if it also is for essential maintenance to assure

efficient operation. These bypasses are not subject to the provision of paragraphs (C) and

(D) of this section.

C.  Bypass Notifications

(1)    If a user knows in advance of the need for a bypass, it shall submit prior notice to

the Superintendent, at least ten (10) days before the date of the bypass, if

possible.

(2)  A user shall submit oral notice to the Superintendent of an unanticipated

bypass that exceeds applicable pretreatment standards within twenty-four

(24) hours from the time it becomes aware of the bypass. A written submission

shall also be provided within five (5) days of the time the user becomes aware of

the bypass. The written submission shall contain a description of the bypass and

its cause; the duration of the bypass, including exact dates and times, and, if the

bypass has not been corrected, the anticipated time it is expected to continue; and

steps taken or planned to reduce, eliminate, and prevent reoccurrence of the

bypass. The Superintendent may waive the written report on a case-by-case basis

if the oral report has been received within twenty-four (24) hours.

D.  Bypass

(1)	Bypass is prohibited, and the Superintendent may take an enforcement

action against a user for a bypass, unless

(a) Bypass was unavoidable to prevent loss of life, personal injury, or severe

property damage;

(b) There were no feasible alternatives to the bypass, such as the use of auxiliary

treatment facilities, retention of untreated wastes, or maintenance during

normal periods of equipment downtime. This condition is not satisfied if

adequate back-up equipment should have been installed in the exercise of

reasonable engineering judgment to prevent a bypass which occurred during

normal periods of equipment downtime or preventive maintenance; and

(c) The user submitted notices as required under paragraph (C) of this section.

(2) The Superintendent may approve an anticipated bypass, after considering its

adverse effects, if the Superintendent determines that it will meet the three

conditions listed in paragraph (D)(1) of this section.

SECTION 14 - MISCELLANEOUS PROVISIONS

14.1	Pretreatment Charges and Fees

The City may adopt reasonable fees for reimbursement of costs offsetting up and operating

the City's Pretreatment Program which may include:

A. Fees for wastewater discharge permit applications including the cost of processing such

applications:

B. Fees for monitoring, inspection, and surveillance procedures including the cost of

collection and analyzing a user's discharge, and reviewing monitoring reports submitted

by users:

C. Fees for reviewing and responding to accidental discharge procedures and construction;

D. Fees for filing appeals: and

E. Other fees as the City may deem necessary to carry out the requirements contained

herein. These fees relate solely to the matters covered by this ordinance and are separate

from all other fees, fines, and penalties chargeable by the City.

14.2       Long-Term Contracts

Nothing in this Ordinance shall prevent the Superintendent from entering into long-term

contracts with any user or industrial user to treat such user's or industrial user's wastewater

discharge to the P0TW, upon advance approval by the City Council. Any such long-term contracts shall not supersede any pretreatment standard, or requirement established under this Ordinance or any Permits issued to a significant Industrial User pursuant to this Ordinance.

14.3	Severability

If any provision of this ordinance is invalidated by any court of competent jurisdiction, the

remaining provisions shall not be effected and shall continue in full force and effect.

14.4     Conflict

All other Ordinances and other parts of Ordinances inconsistent or conflicting with any part

of this Ordinance are hearty repealed to the extent of such inconsistency and or conflict.

14.5	Compliance Date

Compliance with all of the terms and provisions of this Ordinance shall commence April 1,

1995. Compliance with all of the terms and provisions of this Ordinance pertaining to

wastewater discharge permits shall commence when a wastewater discharge permit has been

issued, even though such permit shall require the user to whom said permit was issued to

undertake certain additional pretreatment measures within a time certain as provided in said

permit.

14.6       Appeal Procedure to City Council

Where this Ordinance provides for an appeal to the City Council, the City council may itself

conduct a hearing and take the evidence, or may designate any of its members or its attorney to;

A.	 Issue in the name of the City Council notes of hearings requesting the attendance and

testimony of witnesses and the production of evidence relevant to any manner involved

in such hearing;

B.	Take the evidence;

C.	Transmit a report of the evidence and hearing, including transcripts and other evidence,

together with recommendations to the City Council for action thereon.

SECTION 15 - EFFECTIVE DATE

This ordinance shall be in full force and effect immediately following its passage, approval, and publication in pamphlet form, as provided by law.

Upon roll call vote the following Alderpersons voted aye:

Upon roll call vote the following Alderpersons voted nay:

Passed, approved and published in pamphlet form this 13th day of October, 2020.

ROGER PETHTEL, Mayor

ATTEST:

Sandrea Anderson, City Clerk