CHAPTER 8

SEWER USE

8.01 DEFINITIONS.  Terms used in this chapter (and in Chapter 7 and Chapter 9) mean as follows:

Authority:  The City of Robinson.

Biochemical Oxygen Demand (BOD):  The quantity of oxygen, expressed in mg/1, utilized in the biochemical oxidation of organic matter under standard laboratory procedures in 5 days at 20 degrees C.

Building Drain:  That part of the lowest horizontal piping of a drainage system which receives the discharge from soil, waste and other drainage pipes inside the walls of a building and conveys it to the building sewer beginning 3 feet outside the building wall.

Building Drain, Sanitary:  A building drain which conveys sanitary or industrial sewage only.

Building Drain, Storm:  A building drain which conveys storm water or other clearwater drainage, but no wastewater.

Building Sewer:  The extension from the building drain to the public sewer or other place of disposal (also called house connection).

Building Sewer, Sanitary:  A building sewer which conveys sanitary or industrial sewage only.

Building Sewer, Storm:  A building sewer which conveys stormwater or other clearwater drainage, but no sanitary or industrial sewage.

Class of Users:  The division of wastewater treatment customers by waste characteristics, and process or discharge similarities.  (These definitions are for sewer use control. )

Residential:  Shall include all dwelling units such as detached, semidetached, and row houses, mobile homes, garden and standard apartments, permanent multi-family dwellings. (Transit lodging, considered commercial in nature, is not included.)

Commercial:  Shall include transient lodging retail and wholesale establishments or places engaged in selling merchandise for personal, household or industrial consumption, and/or rendering services to others.

Institutional:  Shall include social, charitable, religious, and educational activities such as schools, churches, hospitals, nursing homes, penal institutions and similar institutional users.

Governmental:  Shall include legislative, judicial, administrative, and regulatory activities or federal, state and local governments, such an courthouses, police and fire stations, city halls, and similar governmental users.

Industrial:  Shall include manufacturing activities involving the mechanical or chemical transformation of materials or substances into other products.  These activities occur in establishments usually described as plants, factories or mills and characteristically use power-driven machines and material handling equipment.

Combined Sewage:  A combination of both wastewater and storm or surface water.

Combined Sewer:  A sewer intended to receive both wastewater and storm or surface water.

Compatible Pollutant:  Biochemical Oxygen Demand, suspended solids, pH, and fecal coliform bacteria, plus additional pollutants identified in the NPDES Permit if the treatment works was designed to treat such pollutants, and in fact does remove such pollutants to a substantial degree.  The term substantial degree is not subject to precise definition, but generally contemplates removals in the order of 80 percent or greater.  Minor incidental removals in the order of 10 to 30 percent are not considered substantial.  Examples of the additional pollutants which may be considered compatible include: (a) chemical oxygen demand, (b) total organic carbon, (c) phosphorus and phosphorus compounds, (d) nitrogen and nitrogen compounds, and (e) fats, oils, and greases of animal or vegetable origin (except as prohibited where these materials would interfere with the operation of the treatment works).

Depreciation:  An annual operating cost reflecting capital consumption and obsolescence (reduction of future service potential) of the treatment works.

Easement:  An acquired legal right for the specific use of land owned by others.

Fecal Coliform:  Any of a number of organisms common to the intestinal tract of man and animals, whose presence in sanitary sewage is an indicator of pollution.

Floatable Oil:  Oil, fat, or grease in a physical state, such that will separate by gravity from wastewater by treatment in a pretreatment facility approved by the authority.

Garbage:  Solid wastes from the domestic and commercial preparation, cooking, and dispensing of food, and from the commercial handling, storage and sale of produce.

Incompatible Pollutant:  Any pollutant that not defined as a compatible pollutant, including non-biodegradable dissolved solids.

Industrial Cost Recovery:  Recovery from the industrial users of a treatment works of the grant amount allocable to treatment of wastes from such users pursuant to Section 204(b) of PL 92-500 and 40 CFR Part 35.928 (1) and (2).

Infiltration:  The water entering a sewer system, including building drains and sewers, from the ground, through such means as, but not limited to, defective pipes, pipe joints, connections, or manhole walls.  (Infiltration does not include and is distinguished from inflow.)

Infiltration/Inflow:  The total quantity of water from both infiltration and inflow without distinguishing the source.

Inflow:  The water discharge into a sewer system, including building drains and sewers, from such sources as, but not limited to, roof leaders, cellar, yard and area drains, foundation drains, unpolluted cooling water discharges, drains from springs and swampy areas, manhole covers, cross connections from storm sewers and combined sewers, catch basins, storm waters, surface runoff, street wash waters or drainage.  (Inflow does not include, and is distinguished from, infiltration.)

Natural Outlet:  Any outlet, including storm sewers and combined sewer overflows, into a watercourse, pond, ditch, lake, or other body of surface or groundwater.

Normal Domestic Sewage:  As defined for the purposes of determining surcharge, shall mean wastewater or sewage having an average daily suspended solids loading of not more than

.20 lbs/TSS/PE, and average daily BOD loading of not more than 0.17 lbs/BOD/PE.

NPDES Permit:  A permit issued under the National Pollutant Discharge Elimination System for discharge of wastewaters to the navigable waters of the United States pursuant to Section 402 of PL 92-500.

Operation and Maintenance Costs:  All costs, direct and indirect, (other than debt service) necessary to insure adequate wastewater treatment on a continuing basis, conform with at related federal, state and local requirements, and assure optimal long term facility management.  (These costs include depreciation and replacement.)

Person:  Any individual, firm, company, association, society, corporation or group discharging any wastewater to the wastewater collection system.

pH:  The reciprocal of the logarithm of the hydrogen ion concentration.  The concentration is the weight of hydrogen ions in grams per liter of solution.  Limits of acceptance are 5.0 to 9.5.

Pretreatment:  The treatment of industrial sewage from privately owned industrial sources prior to introduction into a public treatment works or collection system.

Private Sewer:  A sewer which is not owned by a public authority, and which is the responsibility of the property owner to the point of connection to the public authority’s main sanitary sewer line.

Properly Shredded Garbage:  The wastes from the preparation, cooking and dispensing of food that have been shredded to such a degree that all particles will be carried freely under flow conditions normally prevailing in public sewers with no particle greater than 0.50 inch (1.27 centimeters) in any dimension.

Public Authority:  Any governmental agency having jurisdiction by law over construction and use of a wastewater collection or treatment facility.

Public Sewer:  A sewer which is owned and controlled by the public authority and will consist of the following increments.

Collector Sewer:  A sewer whose primary purpose is to collect wastewaters from individual point source discharges.

Interceptor Sewer:  A sewer whose primary purpose is to transport wastewater from collector sewers to a treatment facility.

Force Main:  A pipe in which wastewater is carried under pressure.

Pumping Station:  A station positioned in the public sewer system at which wastewater is pumped to a higher level.

Replacement:  Expenditures for obtaining and installing equipment, accessories or appurtenances which are necessary during the service life of the treatment works to maintain the capacity and performance for which such works were designed and constructed.

Sanitary Sewer:  A sewer which carries sanitary and industrial wastes, and to which storm, surface and groundwater are not intentionally admitted.

Sewage:  The combination of the liquid and water-carried wastes from residences, commercial buildings, industrial plants and institutions (including polluted cooling water).  The three most common types of sewage are:

Sanitary Sewage:  The combination of liquid and water-carried wastes discharged from toilet and other sanitary plumbing facilities.

Industrial Sewage:  A combination of liquid and water-carried wastes, discharged from any industrial establishment, and resulting from any trade or process carried on in that establishment (this shall include the wastes from pretreatment facilities and polluted cooling water).

Combined Sewage:  Wastes including sanitary sewage, industrial sewage, storm water, infiltration and inflow carried to the wastewater treatment facilities by a combined sewer.

“Shall” is mandatory; “May” is permissive.

Significant Industrial User:

(1) A user subject to categorical pretreatment standards; or

(2) A user that:

(a) Discharges an average of ten thousand (10,000) gpd or more of process wastewater to the POTW (excluding sanitary, noncontact cooling, and boiler blowdown wastewater);

(b) Contributes a process wastestream which makes up five (5) percent or more of the average dry weather hydraulic or organic capacity of the POTW treatment plant; or

(c) Is designated as such by the City on the basis that it has a reasonable potential for adversely affecting the POTW’s operation or for violating any pretreatment standard or requirement.

(3) Upon a finding that a user meeting the criteria in Subsection (2) has no reasonable

potential for adversely affecting the POTW’s operation or for violating any

pretreatment standard or requirement, the City may at any time, on its own initiative

or in response to a petition received from a user, and in accordance with procedures

in 40 CFR 403.8(f)(6), determine that such user should not be considered a significant

industrial user.

Slug:  Any discharge of water or wastewater which in concentration of any given constituent or in quantity of flow exceeds for any period of duration longer than 15 minutes more than five times the average 24 hours concentration of flows during normal operation.

Standard Methods:  The laboratory procedures set forth in the latest edition, at the time of analysis, of “Standard Methods for the Examination of Water and Wastewater” prepared and published jointly by the American Public Health Association, The American Water Works Association and the Water Environment Federation.

Storm Sewer:  A sewer for conveying water, ground water or unpolluted water from any source and to which sanitary and/or industrial wastes are not intentionally admitted.

Suspended Solids:  Solids that either float on the surface of, or are in suspension in, water, sewage or other liquids and which are removable by laboratory filtering.

Total Solids:  The sum of suspended and dissolved solids.

Toxic Amount:  Concentrations of any pollutant or combination of pollutants, which upon exposure to or assimilation into any organism will cause adverse effects, such as cancer, genetic mutations, and physiological manifestations, as defined in standards issued pursuant to Section 307(a) of PL 92-500.

Unpolluted Water:  Water of quality equal to or better than the effluent criteria in effect, or water that would not cause violation of receiving water quality standards and would not be benefited by discharge to the sanitary sewers and wastewater treatment facilities provided.

User Charge:  A charge levied on users of a wastewater treatment works for the cost of operation and maintenance of such works pursuant to Section 204(b) of PL 92-500.

Volatile Organic Matter:  The material in the sewage solids transformed to gases or vapors when heated at 550 degrees C. for 15 to 20 minutes.

Wastewater Treatment Works:  The structures, equipment and processes required to collect, transport and treat domestic and industrial wastes and dispose of the effluent and accumulated residual solids.

Water Works:  All facilities for water supply, filtration plant, storage reservoirs, water lines and services, and booster stations for obtaining, treating and distributing potable water.

Watercourse:  A natural or artificial channel for the passage of water either continuously or intermittently.

8.02 USE OF PUBLIC SEWERS REQUIRED.

(a) Disposition of Wastes on Public or Private Property.  It shall be unlawful for any person to place, deposit, or permit to be deposited in any unsanitary manner on public or private property within the City or in any area under the jurisdiction of said city, any human or animal excrement, garbage, or other objectionable waste.

(b) Treatment of Wastes.  It shall be unlawful to discharge to any natural outlet within the City, or in any area under the jurisdiction of said city, any sewage or other polluted waters, except where suitable treatment has been provided in accordance with subsequent provisions of this chapter.

(c) Privies and Septic Tanks.  Except as hereinafter provided, it shall be unlawful to construct or maintain any privy, privy vault, septic tank, cesspool, or other facility intended or used for the disposal of sewage.

(d) Connection to Sewer.  The owner of all houses, buildings, or properties used for human occupancy, employment, recreation, or other purposes, situated within the city and abutting on any street, alley, or right-of-way in which there is now located or may in the future be located a public sanitary or combined sewer of the city, is hereby required at his expense to install suitable toilet facilities therein, and to connect such facilities directly with the proper public sewer in accordance with the provisions of this chapter, within 90 days after date of official notice to do so, provided that said public sewer is within 100 feet (30 meters) of the property line.  (Rule 2.04 of 1974 Edition of “Private Sewage Disposal Licensing Act and Code”.)

(e) Sewer Connection Deposit.  Prior to the commencement of the use of the public sewer, the proposed user, other than an owner, shall pay unto the City a deposit of $75.00.  Said deposit shall be refunded to said user, without interest, after two years, or in the event sewer use service is voluntarily terminated by the user, and after a waiting period of 45 days, provided, however, that at the time said user is not delinquent to the City in payment of sewer use charges.  (2008-O-36)

8.03 PRIVATE SEWAGE DISPOSAL.

(a) Required.  Where a public sanitary or combined sewer is not available under the provisions of Section 8.02(d), the building sewer shall be connected to a private sewage disposal system complying with the provisions of this section.

(b) Permit.  Before commencement of construction of a private sewage disposal system, the owner shall first obtain a written permit signed by the Mayor.  The application for such permit shall be made on a form furnished by the city (reference Ch. 8 appendix) which the applicant shall supplement by any plans, specifications, and other information as are deemed necessary by the City Council.

A permit and inspection fee of $50 shall be paid to the city at the time the application is filed.

(c) Inspections.  A permit for a private sewage disposal system shall not become effective until the installation is completed to the satisfaction of the City and the local Public Health Department.  The City shall be allowed to inspect the work at any stage of construction and, in any event, the applicant for the permit shall notify the City’s Wastewater Treatment Superintendent when the work is ready for final inspection, and before any underground portions are covered.  The inspection shall be made within sixty (60) hours of the receipt of notice by the City’s Wastewater Treatment Superintendent.

(d) Specifications.  The type, capacities, location, and layout of a private sewage disposal system shall comply with all recommendations of the State of Illinois Private Sewage Disposal Licensing Act and Code and with the State of Illinois Environmental Protection Agency. No permit shall be issued for any private facilities where the area of the lot has insufficient area to meet the recommendations in above mentioned Act and Code.  No septic tank or cesspool shall be permitted to discharge to any natural outlet.

(e) Connection to Sewer.  At such time as a public sewer becomes available to a property served by a private sewage disposal system as provided in Section 8.02, a direct connection shall be made to the public sewer in compliance with this chapter, and any septic tanks, cesspools, and similar private sewage disposal facilities shall be abandoned and filled with suitable material.

(f) Maintenance.  The owner shall operate and maintain the private sewage disposal facilities in a sanitary manner at all times and at no expense to the city.

(g) Additional Regulations.  No statement contained in this section shall be construed to interfere with any additional requirements that may be imposed by the Local Health Officer or other regulatory agencies.

(h) Time for Sewer Connection.  When a public sewer becomes available, the building sewer shall be connected to said sewer within 60 days and the private sewage disposal system shall be cleaned of sludge and filled with suitable material.

8.04 BUILDING SEWERS AND CONNECTIONS.

(a) Permit Required.  No unauthorized person shall uncover, make any connections with, or opening into; use, alter; or disturb any public sewer or appurtenance thereof without first obtaining a written permit from the city.

(b) Wastewater Standards.  All disposal by any person into the sewer system is unlawful except those discharges in compliance with federal standards promulgated pursuant to the Federal Act and more stringent state and local standards.

(c) Classes of Permits; Fees.  Classes of building permits and fees shall be as set forth in Section 7.04.

(d) Conditions for Permit.  A building sewer permit will only be issued and a sewer connection shall only be allowed if it can be demonstrated that the downstream sewerage facilities, including sewers, pump stations and wastewater treatment facilities have sufficient reserve capacity to adequately and efficiently handle the additional anticipated waste load.

(e) Cost of Installation and Connection.  All costs and expense incident to the installation and connection of the building sewer shall be borne by the owner.  The owner shall indemnify the city from any loss or damage that may directly or indirectly be occasioned by the installation of the building sewer.

(f) Separate Connection Each Building.  A separate and independent building sewer shall be provided for every building; except that where one building stands at the rear of another on an interior lot and no private sewer is available or can be constructed to the rear building through an adjoining alley, court, yard, or driveway, the building sewer from the front building may be extended to the rear building and the whole considered as one building sewer.

(g) Old Sewers, Reuse.  Old building sewers may be used on connection with new buildings only when they are found, on examination and test by the city, to meet all requirements of this chapter.

(h) Methods and Materials.  The size, slope, alignment, materials of construction of a building sewer, and the methods to be used in excavating, placing of the pipe, jointing, testing, and backfilling the trench, shall all conform to the requirements of the building and plumbing code or other applicable rules and regulations of the city.  In the absence of code provisions or in amplification thereof, the materials and procedures set forth in appropriate specifications of the American Society of Testing Materials, Water Environment Federation Manual of Practice No. 9, and Standard Specifications for Water and Sewer Main Construction in Illinois shall apply, using the Illinois Plumbing Code as a guide.

(i) Elevation.  Whenever possible, the building sewer shall be brought to the building at an elevation below the basement floor.  In all buildings in which any building drain is too low to permit gravity flow to the public sewer, sanitary sewage carried by such building drain shall be lifted by a means which is approved in accordance with subsection (b) of this section, and discharged to the building sewer.

(j) Surface Water Drainage.  No person shall make connection of roof downspouts, exterior foundation drains, areaway drains, or other sources of surface runoff or groundwater to a building sewer or building drain which in turn is connected directly or indirectly to a public sanitary sewer.

(k) Connections to Conform to Codes.  The connection of the building sewer into the public sewer shall conform to the requirements of the building and plumbing code or other applicable rules and regulations of the city, or the procedures set forth in appropriate specifications of the American Society of Testing Materials, Water Environment Federation Manual of Practice No. 9, and Standard Specifications for Water and Sewer Main Construction in Illinois.  All such connections shall be made gastight and watertight.  Any deviation from the prescribed procedures and materials must be approved by the city before installation.

(l) Inspection.  The applicant for the building sewer permit shall notify the City’s Wastewater Treatment Superintendent when the building sewer is ready for inspection and connection to the public sewer, The connection shall be made under the supervision of the Mayor or his representative.

(m) Excavation; Protection.  All excavations for building sewer installation shall be adequately guarded with barricades and lights so as to protect the public from hazard.  Streets, sidewalks, parkways, and other public property disturbed in the course of the work shall be restored in a manner satisfactory to the city.

(n) Building Sewer Cleaning and Testing.  All building sewers shall be installed in such fashion and with such materials so as to prevent blowout, blowback, or other damage to the building sewers during testing, maintenance and cleaning of the public sewer with machinery and apparatus exerting force upon said building sewer at pressure normally required for cleaning and testing under this Section.

(o) Building Sewer Requirements.

1.  No building sewer shall be less than four (4) inches in diameter.

2.  All building sewers shall be constructed of either cast iron, vitrified clay tile, or

schedule 40 PVC pipe the entire distance to connection with the City's Sewer Main.

3.  It is required that the necessary amount of sand be placed under the building sewer

to ensure proper grade as well as deflection restriction.  Sand shall also be used to

fill the trench line to the top of the building sewer (the complete distance to

connection with the City's sewer main) at a minimum.  (Under no circumstance is it

acceptable to use any other fill material under, or around a building sewer other            than sand.)

4.  A fall of 1/4" per foot is required on a 4" building sewer.  (890.220)

5.  A four inch (4") riser (clean out) is required on all building sewers, close to the

building, at ground level, and equipped with a water tight cap.

6.  If a building sewer is required to extend either in, or partially through a travel way,

that portion which extends in, or through shall be backfilled entirely with sand               except for the necessary road materials as specified by the City's Street Standards.

7.  All building sewer taps/saddles into the main shall be provided by the City

Wastewater Department.  The entire building sewer tap, line installation and/or

replacement shall be inspected by the City's Wastewater Treatment Superintendent

or his designee before being covered.  No line, section of line, or tap shall be

covered up before this inspection/ approval takes place, or the covered section(s)

shall be reexposed at the building sewer owner’s expense.  If, and when the                  building sewer passes inspection by the Superintendent or his designee, the below

mentioned  performance bond will be returned.

8.  The appropriate sewer tap fee and a $ 500.00 performance bond are to be paid to

the City prior to digging.  (If a City street needs to be dug up for part, or all of the

building sewer, the Street Department Superintendent shall be notified by the

building sewer owner in order to set a performance bond amount.)

9.  Any new building sewer which emanates from below basement floor grade shall be

equipped with a proper backflow prevention devise.  Any replacement of an existing

building sewer emanating below basement floor grade shall also be equipped with a

proper backflow prevention devise.

10.  Any re-tap (connection of an existing building sewer tap in another location in close

proximity) shall require a $100.00 re-tap fee.  A performance bond of $500.00 shall

also be paid to the City.  If a retap is made, the abandoned tap must be sealed off

with concrete, mortar or cement.  This must be inspected by the City as well.

11.  Reconnection of an existing building sewer into the same existing tap shall require a

$30.00 fee if the City feels a new saddle is required.  The above listed performance

bond and inspection procedures apply as well on a reconnection.

8.05 STORMWATER DISPOSITION.

(a) No person shall discharge, or cause to be discharged, any stormwater, surface water, groundwater, roof runoff, subsurface drainage, uncontaminated cooling water, or unpolluted industrial process waters to any sanitary sewer.

(b) Stormwater and all other unpolluted drainage shall be discharged to such sewers as are specifically designated as combined sewers or storm sewers, or to a natural outlet approved by the city.  Industrial cooling water or unpolluted process waters may be discharged on approval of the city to a storm sewer, combined sewer, or natural outlet.

8.06 DELETERIOUS WASTES.

(a) No person shall discharge or cause to be discharged any of the following described waters or wastes to any public sewers:

1.  Any gasoline, benzene, naphtha, fuel oil, or other flammable or explosive liquid,

solid, or gas.

2.  Any waters or wastes containing toxic or poisonous solids, liquids, or gases in

sufficient quantity, either singly or by interaction with other wastes, to injure or

interfere with any sewage treatment process, constitute a hazard to humans or

animals, create a public nuisance, or create any hazard in the receiving waters of

the sewage treatment plant.

3.  Any waters or wastes having a pH lower than 5.0 or having any other corrosive

property capable of causing damage or hazard to structures, equipment, and

personnel of the sewage works.

4.  Solid or viscous substances in quantities or of such size capable of causing

obstruction to the flow in sewers, or other interference with the proper operation of

the sewage works such as, but not limited to, ashes, cinders, sand, mud, straw,

shavings, metal, glass, rags, feathers, tar, plastics, wood, unground garbage, whole

blood, paunch manure, hair and flashings, entrails and paper dishes, cups, mild

containers, etc., either whole or ground by garbage grinders.

(b) No person shall discharge or cause to be discharged the following described substances, materials, waters, or wastes if it appears likely in the opinion of the city that such wastes can harm either the sewers, sewage treatment process, or equipment; have an adverse effect on the receiving stream; or can otherwise endanger life, limb, public property, or constitute a nuisance.  In forming its opinion as to the acceptability of these wastes, the city will give consideration to such factors as the quantities of subject wastes in relation to flows and velocities in the sewers, materials of construction of the sewers, nature of the sewage treatment process, capacity of the sewage treatment plant, degree of treatability of wastes in the sewage treatment plant, and maximum limits established by regulatory agencies.  The substances prohibited are:

1.  Any liquid or vapor having a temperature higher than 150 degrees Fahrenheit, (65 degrees C.).

2.  Any waters or wastes containing toxic or poisonous materials; or oils, whether emulsified or not, in excess of 100 mg/1 or containing substances which may solidify or become viscous at temperatures between 32 and 150 degrees Fahrenheit (0 and 65 degrees C).

3.  Any garbage that has not been properly shredded.  The installation and operation of any garbage grinder equipped with a motor of 3/4 horsepower (0.76 hp metric) or greater shall be subject to the review and approval of the city.

4.  Any waters or wastes containing strong acid, iron pickling wastes, or concentrated plating solutions, whether neutralized or not.

5.  Any waters or wastes containing iron, chromium, copper, zinc, or similar objectionable or toxic substances; or wastes exerting an excessive chlorine requirement to such degree that any such material received in the composite sewage at the sewage treatment works exceeds the limits established by the city for such materials, The limits on toxic substances shall be no less stringent than those established by state and federal regulations.

6.  Any waters or wastes containing phenols or other taste or odor-producing substances in such concentrations exceeding limits which may be established by the city as necessary, after treatment of the composite sewage, to meet the requirements of the state, federal, or other public agencies of jurisdiction for such discharge to the receiving waters.

7.  Any radioactive wastes or isotopes of such half-life or concentration as may exceed limits established by the city in compliance with applicable state or federal regulations.

8.  Any waters or wastes having a pH in excess of 9.5.

9.  Any mercury or any of its compounds in excess of 0.005 mg/L as permitted by the city in compliance with applicable state and federal regulations

10.  Any cyanide in excess of 1.6 mg/L at any time except as permitted by the city in compliance with applicable state and federal regulations.

11.  Materials which exert or cause:

A.  Unusual concentrations of inert suspended solids (such as, but not limited to, Fullers earth, lime slurries, and lime residues) or of dissolved solids (such as, but not limited to, sodium chloride and sodium sulfate);

B.  Excessive discoloration (such as, but not limited to, dye wastes and vegetable tanning solutions);

C.  Unusual BOD, chemical oxygen demand, or chlorine requirements in such quantities as to constitute a significant load on the sewage treatment works;

D.  Unusual volume of flow our concentrations of wastes constituting “slugs” as defined herein.

12.  Waters or wastes containing substances which are not amenable to treatment or reduction by the sewage treatment processes employed, or are amenable to treatment only to

such degree that the sewage treatment plant effluent cannot meet the requirements of agencies having jurisdiction over discharge to the receiving waters.

8.07 DISPOSITION OF DELETERIOUS WASTES.

(a) If any waters or wastes are discharged, or are proposed to be discharged to the public sewers, which waters contain the substances or possess the characteristics enumerated in Section 8.06 (c) and/or which are in violation of the standards for pretreatment provided in Chapter 1, EPA Rules and Regulations, subchapter D, Water Programs Part 128-Pretreatment Standards, Federal Register Volume 38, No. 215, Thursday, November 8, 1973 and any amendments thereto, and which in the judgment of the city may have a deleterious effect upon the sewage works, processes, equipment, or receiving waters, or which otherwise create a hazard to life or constitute a public nuisance, the city may:

1.  Reject the wastes;

2.  Require pretreatment to an acceptable condition for discharge to the public sewers;

3.  Require control over the quantities and rates of discharge; and/or

4.  Require payment to cover the added costs of handling and treating the wastes not covered by existing taxes or sewer charges, under the provisions of Section 8.10.

(b) If the city permits the pretreatment or equalization of waste flows, the design and installation of the plants and equipment shall be subject to the review and approval of the city, and subject to the requirements of all applicable codes, ordinances, and laws.

(c) Where preliminary treatment or flow-equalizing facilities are provided, they shall be maintained continuously in satisfactory and effective operation by the owner at his expense. These facilities shall be accessible for inspection by the city.

8.08 INTERCEPTORS.  Grease, oil, and sand interceptors shall be provided when, in the opinion of the city they are necessary for the proper handling of liquid wastes containing grease in excessive amounts, or any flammable wastes, sand, or other harmful ingredients; except that such interceptors shall not be required for private living quarters or dwelling units. All interceptors shall be of a type and capacity approved by the city, and shall be located as to be readily and easily accessible for cleaning and inspection.  All interceptors shall be cleaned at intervals which allow proper acceptable removal efficiencies as determined by the interceptor manufacturer.

8.09 CONTROL MANHOLES.  Each new industry shall be required to install a control manhole and, when required by the city, the owner of any property serviced by a building sewer carrying industrial wastes shall install a suitable control manhole, together with such necessary meters an other appurtenances in the building sewer to facilitate observation, sampling, and measurement of the wastes.  Such manhole, when required, shall be accessibly and safely located, and shall be constructed in accordance with plans approved by the city.  The manhole shall be installed by the owner at his expense, and shall be maintained by him so as to be safe and accessible at all times.

8.10 LABORATORY TESTS OF WASTES.  The owner of any property serviced by a building sewer carrying industrial wastes shall provide laboratory measurements, tests, and analyses of waters and wastes to illustrate compliance with this chapter and any special conditions for discharge established by the city or regulatory agencies having jurisdiction over the discharge.

The number, type, and frequency of laboratory analyses to be performed by the owner shall be as stipulated by the city, but no less than once per year the industry must supply a complete analysis of the constituents of the wastewater discharge to assure that compliance with the federal, state, and local standards are being met.  The owner shall report the results of measurements and laboratory analyses to the city at such times and in such manner as prescribed by the city.  The owner shall bear the expense of all measurements, analyses, and reporting required by the city.  At such times as deemed necessary, the city reserves the right to take measurements and samples for analysis by an outside laboratory service.

8.11 TESTS AND MEASUREMENT STANDARDS.  All measurements, tests, and analyses of the characteristics of waters and wastes to which reference is made in this chapter shall be determined in accordance with the latest edition of “Standard Methods for the Examination of Water and Wastewater,” published by the American Public Health Association, and the October 16, 1973 Federal Register (40 CFR Part 136 entitled “Guide lines Establishing Test Procedures for Analysis of Pollutants”) and shall be determined at the control manhole provided, or upon suitable sample taken at said control manhole.  In the event that no special manhole has been required, the control manhole shall be considered to be the nearest downstream manhole in the public sewer to the point at which the building sewer is connected. Sampling shall be carried out by customarily accepted methods to reflect the effect of constituents upon the sewage works and to determine the existence of hazards to life, limb, and property (The particular analyses involved will determine whether a 24 hour composite of all outfalls of a premise is appropriate or whether a grab sample or samples should be taken. Normally, but not always, BOD and suspended solids analyses are obtained from 24-hour composites of all outfalls, whereas pH’s are determined from periodic grab samples.)

8.12 AGREEMENTS FOR TREATMENT OF WASTES.  No statement contained in this chapter shall be construed as preventing any special agreement or arrangement between the city and any industrial concern whereby an industrial waste of unusual strength or character may be accepted by the city for treatment, subject to payment therefor, in accordance with Section 9.02 of this code, by the industrial concern, provided such payments are in accordance with federal and state guidelines for User Charge System and Industrial Cost Recovery System.

8.13 PROTECTION OF SEWAGE WORKS FROM DAMAGE.  No unauthorized persons shall maliciously, willfully, or negligently break, damage, destroy, or tamper with any structure, appurtenance, or equipment which is a part of the sewage works.  Any person violating this provision shall be subject to immediate arrest under charge of disorderly conduct.

No unauthorized person shall conduct any excavating within 10 feet of any sanitary sewer within the city, without first having notified the Wastewater Treatment Superintendent at least 24 hours prior to the commencement of such excavating.  No excavating shall progress until such time that the Wastewater Treatment Superintendent, or his representative, has inspected the proposed excavation and issued a permit in writing for it.  Any person violating this provision shall be subject to immediate arrest under charge of disorderly conduct.

(83-0-32)

8.14 POWERS AND AUTHORITY OF INSPECTORS.

(a) Entry on to Premises.  The Mayor and other duly authorized employees of the city, the Illinois Environmental Protection Agency, and the U.S. Environmental Protection Agency, bearing proper credentials and identification, shall be permitted to enter all properties for the purposes of inspection, observation, measurement, sampling, and testing in accordance with the provisions of this chapter.

(b) Liability of Sewer User.  While performing the necessary work on private properties referred to in subsection (a) above, the Mayor or duly authorized employees of the city, the Illinois Environmental Protection Agency, and the U.S. Environmental Protection Agency shall observe all safety rules applicable to the premises established by the company and the company shall be held harmless for injury or death to the city employees and the city shall indemnify the company against loss or damage to its property by city employees and against liability claims and demands for personal injury or property damage asserted against the company and growing out of the gauging and sampling operation, except as such may be caused by negligence or failure of the company to maintain safe conditions as required in Section 8.09.

(c) Credentials and Rights to Inspect.  The Mayor and other duly authorized employees of the city bearing proper credentials and identification shall be permitted to enter all private properties through which the city holds a duly negotiated easement for the purposes of, but not limited to, inspection, observation, measurement, sampling, repair, and maintenance of any portion of the sewage works lying within said easement.  All entry and subsequent work, if any, on said easement, shall be done in full accordance with the terms of the duly negotiated easement pertaining to the private property involved.

8.15 SEWER USE CHARGES.

(a) Rates.  There shall be and there are hereby established rates and charges for the use of and for the service of the sewerage system of the City.  Such rates or charges shall be based upon the classification of the user as residential, commercial, or industrial, and upon the amount of water supplied by the Robinson-Palestine Water Commission, as shown by the monthly water meter readings or measured effluent to the sewer system shall be charged the rate hereafter set out based on the water meter readings or the measured effluent as follows:

1.   a.  Residential

WATER USAGE	MINIMUM FEE

0-100 cubic feet	$10.00

over 100 cubic feet	$2.00 per 100 cubic feet

b.  Commercial

WATER USAGE	MINIMUM FEE

0-300 cubic feet	$12.00

Over 300 cubic feet	$2.00 per 100 cubic feet

c.  Industrial

WATER USAGE	MINIMUM FEE

0-300 cubic feet	$150.00

Over 300 cubic feet	$2.00 per 100 cubic feet

2.  In all cases in which users of said sewerage system are not supplied with water from the Robinson-Palestine Water Commission System, the charge for the use of the sewerage system shall be a minimum of $20.00 per month or a fraction thereof.  (86-0-12)

(b) Meters.  A user of the sewerage system of the City shall, at his cost and option, either install a device to measure the effluent being discharged into said sewerage system, or so arrange his water meters to separately meter the water supplied from the Robinson-Palestine Water Commission System that is being discharged into said sewerage system, after same shall have been approved by the City upon recommendation of the City Engineers.  When the effluent being discharged into said sewerage system is measured, then the rates and charges to said users shall be based upon the measured effluent rather than upon the monthly water meter readings of the Robinson-Palestine Water Commission.  When the user shall separately meter the water supply being discharged into said sewerage system, then the rates and charges to said user shall be based upon the monthly water meter readings of those meters of the Robinson-Palestine Water Commission supplying water which is discharged into said sewerage system.  The Mayor of the City, or his duly authorized representative shall have access to the premises of the user at reasonable times and intervals for the purpose of inspecting and observing the measurement of effluent being discharged into said sewerage system pursuant to said provision.  (85-0-06)

(c) Premises Outside City.  Whenever premises located outside of the corporate boundaries of the City are connected to the sewerage system of the city and are provided service by said system, rates and charges for the particular service rendered shall be equal to the rates and charges as set out in subsection (a) times 150%.

The user shall keep accurate records of any cleaning or maintenance of

wastewater flow measurement systems and shall have the accuracy and totalizer reading of the system checked and noted on a regular basis.  All parts of the system which require cleaning to maintain meter accuracy shall be cleaned at the manufacturer’s suggested frequency and/or the interval required herein.  The “zero level” of the indicator and recorder shall be verified each time to ensure that the flows are recorded correctly.

All flow monitoring systems used to obtain flow information for submittal to the

City shall have the calibration of the system inspected quarterly.  The quarterly

calibration inspections may be instrumentation calibrations.  The instrumentation calibration shall confirm that the actual flow rates are accurately measured by the primary measuring device and transmitted to the flow recorder and totalizer.  The instrumentation shall be checked at three flow rates covering the normal range of operation.  A summary of the calibration shall be recorded.

The flow measurement system maintenance and calibration records shall be

maintained by the user and shall be made available upon request to

representatives of the City. (09-O-01)

(d) Billing.  Rates and charges for service shall be based upon monthly usage, but shall be due monthly.  The owner of the premises, the occupant thereof, and the use of the service shall be jointly and severally liable to pay for the service on said premises, and the service is furnished to the premises by the City only upon the condition that the owner of the premises, occupant and user of the service are jointly and severally liable therefor to the City.  All bills for service shall be rendered as of the 15th day of the month succeeding the period for which the service is billed, and shall be payable not later than the close of business on the 28th day of the same month.  A penalty of five (5) percent shall be added on all bills not paid by the 28th day of the same month.  When the 28th day of any month shall be a Sunday or a legal holiday, then such bills for service shall be payable on the next succeeding secular day without the penalty added.  In addition, there shall be imposed on each delinquent bill a service charge of Ten Dollars ($10.00) for each delinquency notice.  (08-O-24)

(e) Delinquent.  In the event the charges for service are not paid for within 60 days after rendition of the bill for such service, such charges shall be deemed and are hereby declared to be delinquent, and thereafter such delinquencies shall constitute liens on the real estate for which service is supplied, and the City Clerk is hereby authorized and directed to file from time to time as directed by the City Council, sworn, detailed statements showing such delinquencies in the office of the Recorder of Deeds of Crawford County, and the filing of such statements shall be deemed notice of lien for payment of the service rendered.

(f) Discontinuing Service.  If the rates or charges for such service are not paid within 60 days after rendition of the bill for such service, the City may discontinue sewerage service by the disconnection of the service line or lines from the premises being served by such service from the City’s sewer lines, after the procedures as set forth hereinafter have been followed:

1.  The City shall give written notice to the user of the service and the owner of the premises to which the service was provided, that the delinquency exists, and that a lien as provided by law, shall be filed for the delinquent charges after 10 days from the date of the notice.

2.  After the lien on the real estate for which service was supplied has been filed, a true and correct copy of it shall be sent to the user of the service and the owner of the premises to which the service was provided, along with a notice that a disconnection of sewerage service and a disconnection from the sewer system shall occur after 30 days from the date of the notice.

3.  After 30 days from giving the written notice of a disconnection of sewer service and a disconnection of service from the sewer system, the user of the service and owner of the premises to which the service was provided, shall be given a written notice of disconnection, advising of the liability of the user and the owner of the premises for the costs involved in disconnection and the costs required for a reconnection to the sewer system.

4.  Not less than 15 days prior to disconnection of sewer service, and a disconnection from the sewer system of the City, the user and the owner of the premises to which sewer

service was supplied, shall be given written notice of the date after which disconnection shall occur.

Once sewer service has been discontinued, and there has been a disconnection of the service, as provided for herein above, then, prior to the reconnection of the premises to which the disconnection of service and a disconnection has occurred, there shall first be paid to the City its actual costs of disconnection of sewer service, its actual costs of reconnection of sewer service, both amounts as calculated by the Superintendent of the Waste Water Treatment System, and, in addition thereto, a reconnection fee of $200, and a deposit equal to one year’s sewer use charges as computed by the Superintendent.

(g) Leaks.  In the event of a water leak wherein it can be established to the city that said water did not enter the sewerage system, then the charges as provided herein shall be reduced in accordance with reductions of charges for water supplied by the Robinson-Palestine Water Commission.

(h) Recording.  A copy of this section, properly certified by the City Clerk, shall be filed in the office of the Recorder of Deeds in Crawford County and shall be deemed notice to all owners of real estate of their liability for service supplied to any user of the service of the sewerage system of the city on their properties, and it shall be the duty of the City Clerk and such other officers of the city to take all actions necessary or required by the laws of the State of Illinois thereunto enabling to file all claims for money due to the city and to prosecute and

enforce such claims in the manner, form and time as permitted by the laws of the State of Illinois.

(i) Sewer Use Restrictions.  In the event a sewer use charge shall remain unpaid and past due for a specific sewer use hookup location, then, in the event there shall be a request for a charge in user and occupancy of the premises to which said sewer use service has heretofore been provided, then, no change in user and occupier shall be permitted until such time that said unpaid sewer use charges and penalties have been paid in full.

8.16 PENALTIES.

(a) Any person found to be violating any provision of this chapter except Section 8.13 shall be served by the city with written notice stating the nature of the violation and providing a reasonable time limit for the satisfactory correction thereof.  The offender shall, within the period of time stated in such notice, permanently cease all violations.  The city may revoke any permit for sewage disposal as a result of any violation of any provision.

(b) Any person who shall continue any violation beyond the time limit provided for in subsection (a) above shall be guilty of a misdemeanor, and on conviction thereof shall be fined as provided in Section 1.06 of this code.

(c) Any person violating any of the provisions of this section shall become liable to the city by reason of such violation.