CHAPTER 23

# FLOOD HAZARD AREAS

23.01 PURPOSE.  This ordinance is enacted pursuant to the police powers granted to this City by the Illinois Compiled Statutes, (Chapter 65, Sections 1-2-1, 11-12-12, 11-30-2, 11-30-8, and 11-31-2) in order to accomplish the following purposes:

(a) to prevent unwise developments from increasing the flood or drainage hazards to others;

(b) to protect new buildings and major improvements to buildings from flood damage;

(c) to protect human life and health from the hazards of flooding;

(d) to lessen the burden on the taxpayer for flood control projects, repairs to flood-damaged public facilities and utilities, and flood rescue and relief operations;

(e) to maintain property values and a stable tax base by minimizing the potential for creating flood blight areas; and

(f) to make federally subsidized flood insurance available for property in the city by fulfilling the requirements of the National Flood Insurance Program.

(g) to preserve the natural characteristics and functions of watercourses and floodplains in order to moderate flood and storm water impacts, improve water quality, reduce soil erosion, protect aquatic and riparian habitat, provide recreational opportunities, provide aesthetic benefits and enhance community and economic development.

23.02 DEFINITIONS.  For the purpose of this ordinance, the following definitions are adopted:

(a) “Flood” means: a general and temporary condition of inundation of normally dry land areas from the overflow, the unusual and rapid accumulation, or the runoff of surface waters from any source.

(b) “Base Flood” means: the flood having a one-percent probability of being equaled or exceeded in any given year.  The base flood is also known as the 100 year flood.  The base flood elevation at any location is as defined in section 23.04 of this ordinance.

(c) “SFHA” or “Special Flood Hazard Area” means: those lands within the jurisdiction of the city that are subject to inundation by the base flood.  The SFHAs of the city are generally identified as such on the Flood Insurance Rate Map of the city prepared by the Federal Emergency Management Agency and dated April 6, 1984.  The SFHAs of those parts of unincorporated Crawford County that are within the extraterritorial jurisdiction of the city or that may be annexed into the city are generally identified as such on the Flood Insurance Rate Map prepared for Crawford County by the Federal Emergency Management Agency and dated June 3, 1986.

(d) “Riverine SFHA” means:  any SFHA subject to flooding from a river, creek, intermittent stream, ditch, or any other identified channel.  This term does not include areas subject to flooding from lakes (except public bodies of water), ponding areas, areas of sheet flow, or other areas not subject to overbank flooding.

(e) “Floodway” means: that portion of the SFHA required to store and convey the base flood.  The floodway for each of the SFHAs of the city shall be according to the best data available to the Illinois State Water Survey Floodplain Information Repository.

(f) “FPE” or “Flood Protection Elevation” means: the elevation of the base flood plus one foot at any given location in the SFHA.

(g) “Development” means: any manmade change to real estate, including:

1.  construction, reconstruction, or placement of a building or an addition to a building valued at more than $1,000;

2.  installing a manufactured home on a site, preparing a site for a manufactured home or installing a travel trailer on a site for more than 180 days;

3.  installing utilities, construction of roads, or similar projects;

4.  construction or erection of levees, walls, fences, bridges or culverts;

5.  drilling, mining, filling, dredging, grading, excavating, or other nonagricultural alterations of the ground surface;

6.  storage of materials; or

7.  any other activity that might change the direction, height, or velocity of flood or surface waters.

“Development” does not include maintenance of existing buildings and facilities such as re-roofing; re-surfacing roads; or gardening, plowing, and similar agricultural practices that do not involve filling, grading, or construction of levees.

(h)  “Building” means: a structure that is principally above ground and is enclosed by walls and a roof.  The term includes a gas or liquid storage tank, a manufactured home, or prefabricated building.  The term includes a travel trailer or recreational vehicle installed on a site for more than 180 days.

23.03 DUTIES OF THE ZONING ADMINISTRATOR.  The Zoning Administrator shall be responsible for the general administration and enforcement of this ordinance, including but not limited to the following duties:

(a) Ensure that all development activities within the SFHAs of the jurisdiction of the city meet the requirements of this ordinance;

(b) Provide information and assistance to citizens upon request about permit procedures and floodplain construction techniques;

(c) Ensure that construction authorization has been granted by the Illinois Department of Transportation, Division of Water Resources for all development projects subject to Section 23.06 of this ordinance, and maintain a record of such authorization;

(d) Maintain a record of the “as built” elevation of the lowest floor (including basement) of all buildings subject to Section 23.07 of this ordinance;

(e) Maintain a record of the engineer’s certificate and the “as built” floodproofed elevation of all buildings subject to Section 23.07(d) of this ordinance;

(f) Inspect all development projects to ensure they comply with the provisions of this ordinance;

(g) Cooperate with state and federal floodplain management agencies to improve base flood and floodway data and to improve the administration of this ordinance.  Submit reports as required for the National Flood Insurance Program; and

(h) Maintain for public inspection and furnish upon request base flood data, SFHA maps, copies of federal or state permit documents and “as built” elevation and floodproofing data for all buildings constructed subject to this ordinance.

23.04 BASE FLOOD ELEVATION.  This ordinance’s protection standard is the base flood.  The best available base flood data is listed below.  Whenever a party disagrees with the best available data, he may finance the detailed engineering study needed to replace existing data with better data and submit it to the State Water Survey and the Federal Emergency Management Agency for approval.

(a) The base flood elevation for each of the SFHAs delineated as an “A Zone” on the Flood Insurance Rate Map of the city shall be according to the best data available to the Illinois State Water Survey Floodplain Information Repository.  When no base flood elevation exists, the base flood elevation shall be the 100 year flood depth calculated according to the formulas presented in Depth & Frequency of Floods in Illinois published by the U.S. Geological Survey, 1976.

(b) The base flood elevation for the SFHAs of those parts of unincorporated Crawford County that are within the extraterritorial jurisdiction of the city or that may be annexed into the city shall be as delineated on the 100 year flood profiles in the Flood Insurance Study of Crawford County prepared by the Federal Emergency Management Agency and dated June 3, 1986.

23.05 DEVELOPMENT PERMIT.  No person, firm, corporation, or other governmental body not exempted by law, shall commence any development in the SFHA without first obtaining a development permit from the Zoning Administrator.  The Zoning Administrator shall not issue a development permit if the proposed development does not meet the requirements of this ordinance.

(a) The application for a development permit shall be accompanied by drawings of the site, drawn to scale showing property line dimensions; existing grade elevations and all changes in grade resulting from excavation or filling; the location and dimensions of all buildings and additions to building; and the elevation of the lowest floor (including basement) of all proposed buildings subject to the requirements of Section 23.07 of this ordinance.

(b) Upon receipt of an application for a development permit, the Zoning Administrator shall compare the elevation of the site to the base flood elevation.  Any development located on land that can be shown to have been higher than the base flood elevation as of the date of the site’s first Flood Insurance Rate Map identification is not located in the SFHA and therefore not subject to the requirements of this ordinance.  The Zoning Administrator shall maintain documentation of the existing ground elevation at the development site and certification that this ground elevation existed prior to the date of the site’s first Flood Insurance Rate Map identification.

(c) The Zoning Administrator shall inform the applicant of any and all other local, state, and federal permits that may be required for this type of development activity.  The Zoning Administrator shall not issue the development permit unless all required federal and state permits have been obtained.

23.06 PREVENTING INCREASED DAMAGES.  No development in the SFHA shall create a damaging or potentially damaging increase in flood heights or velocity or threat to public health and safety.

(a) Within all riverine SFHAs, the following standards shall apply:

(i) In addition to the other requirements of this ordinance, a development permit for a site located in a floodway (or in a riverine SFHA where no floodway has been identified) shall not be issued unless the applicant first obtains a permit or written documentation that a permit is not required from the Illinois Department of Transportation, Division of Water Resources, issued pursuant to 615 ILCS 5/4.9 et seq., as amended.

(ii) The following activities may be constructed without the individual permit required in subsection 23.06(a)(i) in accordance with statewide permits issued by the Illinois Department of Transportation, Division of Water Resources, provided the activities do not involve placement of fill, change of grade, or construction in the normal channel.  Such activities must still meet the other requirements of this ordinance:

(a) The construction of wells, septic tanks, and underground utility lines not crossing a lake or stream;

(b) The construction of light poles, sign posts and similar structures;

(c) The construction of sidewalks, driveways, athletic fields (excluding fences), patios and similar surfaces which are built at grade;

(d) The construction of property anchored, unwalled, open structures such as playground equipment, pavilions, and carports;

(e) The placement of property anchored buildings not exceeding seventy (70) square feet in size, nor ten (10) feet in any dimension (e.g. animal shelters and tool sheds); and

(f) The construction of additions to existing buildings which do not increase the first floor area by more than twenty (20) percent, which are located on the upstream or downstream side of the existing building, and which do not extend beyond the sides of the existing building that are parallel to the flow of flood waters.

(iii) The total cumulative effect of the proposed development, when combined with all other existing and anticipated development, will not increase the base flood elevation more than 1.0 foot for the affected hydraulic reach of the stream and will not increase flood damages or potential flood damages;

(b) Public health standards in all SFHAs.

(i) No development in the SFHA shall include locating or storing chemicals, explosives, buoyant materials, flammable liquids, pollutants, or other hazardous or toxic materials below the FPE unless such materials are stored in a storage tank or flood proofed building constructed according to the requirements of Section 23.07(d) of this ordinance.

(ii) New and replacement sanitary sewer lines and on-site waste disposal systems may be permitted providing all manholes or other above ground openings located below the FPE are watertight.

23.07 PROTECTING BUILDINGS.  In addition to the damage prevention requirements of 23.06, all buildings to be located in the SFHA shall be protected from flood damage below the FPE.  This building protection requirement applies to the following situations:

(i)  construction or placement of a new building valued at more than $1,000;

(ii)  structural alterations made to an existing building that increase the floor area by more than 20%, or the market value of the building by more than 50%;

(iii)  reconstruction or repairs made to a damaged building that are valued at or more than 50% of the value of the building before the damage occurred;

(iv)  installing a manufactured home on a new site or a new manufactured home on an existing site.  This ordinance does not apply to returning a manufactured home to the same site it formerly lawfully occupied before it was removed to avoid flood damage; and

(v)  installing a travel trailer on a site for more than 180 days.

This building protection requirement may be met by any one of the following methods.  The Zoning Administrator shall maintain a record of compliance with these building protection standards as required by Section 23.03 of this ordinance.

(a) A residential or nonresidential building may be constructed on permanent land fill in accordance with the following:

(i)  The fill shall be placed in layers no greater than 1 foot deep before compaction.

(ii)  The lowest floor (including basement) shall be at or above the FPE.  The fill should extend at least ten feet beyond the foundation of the building before sloping below the FPE.

(iii)  The fill shall be protected against erosion and scour during flooding by vegetative cover, rip rap, or bulkheading.  If vegetative cover is used, the slopes shall be no steeper than 3 horizontal to 1 vertical.

(iv)  The fill shall not adversely affect the flow of surface drainage from or onto neighboring properties.

(b) A residential or nonresidential building may be elevated in accordance with the following:

(i)  The building or improvements shall be elevated on stilts, piles, walls, crawl space, or other foundation provided:

(a) the walls have permanent openings no more than one foot above grade; and

(b) the walls and floor are not subject to damages by hydrostatic pressures associated with the base flood.

(ii)  The foundation and supporting members shall be anchored and aligned in relation to flood flows and adjoining structures so as to minimize exposure to known hydrodynamic forces such as current, waves, ice, and floating debris.

(iii)  All areas below the FPE shall be constructed of materials resistant to flood damage.  The lowest floor (including basement) and all electrical, heating, ventilating, plumbing, and air conditioning equipment and utility meters shall be located at or above the FPE.  Water and sewer pipes, electrical and telephone lines, submersible pumps, and other waterproofed service facilities may be located below the FPE.

(c) Manufactured homes and travel trailers to be installed on a site for more than 180 days shall be:

(i) elevated at or above the FPE in accordance with Section 23.07(a) or (b), and

(ii) anchored to resist flotation, collapse, or lateral movement by being tied down in accordance with the Rules and Regulations for the Illinois Mobile Home Tiedown Act, issued pursuant to 210 ILCS 120/1 et seq., as amended.

(d) Only a non-residential building may be flood proofed in accordance with the following:

(i)  A Registered Professional Engineer shall certify that the building has been designed so that below the FPE, the structure and attendant utility facilities are watertight and capable of resisting the affects of the base flood.  The building design shall take into account flood velocities, duration, rate of rise, hydrostatic and hydro-dynamic forces, the effects of buoyancy, and impacts from debris or ice.

(ii)  Flood proofing measures shall be operable without human intervention and without an outside source of electricity.

23.08 OTHER DEVELOPMENT REQUIREMENTS.  The City Council shall take into account flood hazards, to the extent that they are know, in all official actions related to land management, use, and development.

(a) New subdivisions, manufactured home parks, annexation agreements, planned unit developments (PUDs) and additions to manufactured home parks and subdivisions shall meet the requirements of Section 23.06 and 23.07 of this ordinance.  Plats or plans for new subdivisions, manufactured home parks, and planned unit developments (PUDs) shall include a signed statement by a Registered Professional Engineer that the plat or plan accounts for changes in the drainage of surface waters in accordance with the Plat Act (765 ILCS 205/2).

(b) Proposals for new subdivisions, manufactured home parks, planned unit developments (PUDs) and additions to manufactured home parks and subdivisions shall include base flood elevation data.  Where the base flood elevation is not available from an existing study filed with the Illinois State Water Survey, the applicant shall be responsible for calculating the base flood elevation and submitting it to the State Water Survey for review and approval as best available elevation data.

23.09 VARIANCES.  Whenever the standards of this Ordinance place undue hardship on a specific development proposal, the applicant may apply to the Zoning Board of Appeals for a variance.  The Zoning Board of Appeals shall review the applicant’s request for a variance and shall submit its recommendation to the City Council.  The City Council may attach such conditions to granting of a variance as it deems necessary to further the intent of this ordinance.

(a) No variance shall be granted unless the applicant demonstrates that:

(i)  the development activity cannot be located outside the SFHA;

(ii)  an exceptional hardship would result if the variance were not granted;

(iii)  the relief requested is the minimum necessary;

(iv)  there will be no additional threat to public health or safety or creation of a nuisance;

(v)  there will be no additional public expense for flood protection, rescue or relief operations, policing, or repairs to roads, utilities, or other public facilities; and

(vi)  the provisions of subsection 23.06(c) and 23.06(a) of this Ordinance are still met.

(b) The Zoning Administrator shall notify an applicant in writing that a variance from the requirements of 23.07 that would lessen the degree of protection to a building will:

(i)  result in increased premium rates for flood insurance up to amounts as high as $25 for $100 of insurance coverage;

(ii)  increase the risks to life and property; and

(iii)  require that the applicant proceed with knowledge of these risks and that he will acknowledge in writing that he assumes the risk and liability.

(c) Variances to the building protection requirements of 23.07 of this ordinance requested in connection with the reconstruction, repair or alteration of a site or building included on the National Register of Historic Places or the Illinois Register of Historic Places may be granted using criteria more permissive than the requirements of Subsection 23.09(a)(i)-(vi).

23.10 DISCLAIMER OF LIABILITY.  The degree of flood protection required by this Ordinance is considered reasonable for regulatory purposes and is based on available information derived from engineering and scientific methods of study.  Larger floods may occur or flood heights may be increased by man-made or natural causes.  This Ordinance does not imply that development either inside or outside of the SFHA will be free from flooding or damage.  This Ordinance does not create liability on the part of the city or any officer or employee thereof for any flood damage that results from reliance on this Ordinance or any administrative decision made lawfully thereunder.

23.11 PENALTY.  Failure to obtain a permit for development in the SFHA or failure to comply with the requirements of a permit or conditions of a variance resolution shall be deemed to be a violation of this ordinance.  Upon due investigation the Zoning Administrator may determine that a violation of the minimum standards of this ordinance exist.  The Zoning Administrator shall notify the owner in writing of such violation.

(a) If such owner fails after ten days notice to correct the violation, the City may make application to the Circuit Court for an injunction requiring conformance with this Ordinance or make such other Order as the Court deems necessary to secure compliance with the Ordinance.

(b) The Zoning Administrator shall inform the owner that any such violation is considered a willful act to increase flood damages and therefore may cause coverage by the Standard Flood Insurance Policy to be suspended.

(c) Nothing herein shall prevent the City from taking such other lawful action to prevent or remedy any violations.  All costs connected therewith shall accrue to the person or persons responsible.

23.12 ABROGATION AND GREATER RESTRICTIONS.  This Ordinance repeals and replaces other ordinances adopted by the City Council to fulfill the requirements of the National Flood Insurance Program including Ordinance No. 83-O-17.  However, this Ordinance does not repeal the original resolution or ordinance adopted to achieve eligibility in the Program.  Nor does this ordinance repeal, abrogate, or impair any existing easements, covenants, or deed restrictions.  Where this Ordinance and other ordinance easements, covenants, or deed restrictions conflict or overlap, whichever imposes the more stringent restrictions shall prevail.

23.13 SEPARABILITY.  The provisions and sections of this Ordinance shall be deemed separable and the invalidity of any portion of this Ordinance shall not affect the validity of the remainder.

23.14 EFFECTIVE DATE.  This Ordinance shall be in full force and effect from and after its passage and approval and publication, as required by law.